附件 一  船舶接獲特高頻／中頻數位選擇呼叫遇險警報作業流程

Actions by Ships Upon Reception of VHF/MF DSC Distress Alert

# Text boxes

DSC distress alert

is received

接獲DSC遇險呼叫警報

Listen on VHF CH16 / 2182kHz for 5 min

於特高頻無線電話16頻道或中頻2182仟赫頻道上守聽5分鐘

Is the alert acknowled-ged by CS and/or RCC?

該警報是否被海岸電臺及/或搜救協調中心所確認?

No 否

Yes 是

Acknowledge the alert by radiotelephony to the ship in distress on VHF ch16/2182kHz

於特高頻16/中頻2182仟赫頻道上以無線電話確認遇險船舶之警報

Is distress traffic in progress?

遇險通信是否仍在進行?

Inform CS and/or RCC

通知海岸電臺及/或搜救協調中心

Enter details in log  詳情記錄於日誌簿

Reset system

系統重新設定

Is own vessel able to assist?

本船能否提供協助?

Yes 是

No 否

Is the DSC distress call continuing?

數位選擇呼叫遇險呼叫是否仍持續?

Remarks備註：

1. Appropriate or relevant RCC and/or Coast station shall be informed accordingly. If further DSC alerts are received from the same source and the ship in distress is beyond doubt in the vicinity, a DSC acknowledgement may, after consultation with an RCC or Coast Station, be sent to terminate the call.

經通知適當或相關之搜救協調中心及/或海岸電臺後，若持續收到相同且確認來自附近之遇險船舶數位選擇呼叫警報信號，經與搜救協調中心或海岸電臺諮商後，得發送一數位選擇呼叫確認以終止該呼叫。

2. In no case is a ship permitted to transmit a DSC distress relay call on receipt of a DSC distress alert on either VHF channel 70 or MF channel 2187.5kHz.

於特高頻70或中頻2187.5仟赫頻道上接獲數位選擇呼叫遇險警報時，船舶均不准發送數位選擇呼叫之遇險中繼呼叫。

3. CS=Coast Station   RCC=Rescue Co-ordination Center

CS係指海岸電臺  RCC係指搜救協調中心

Yes 是

No 否

Note 1

備註1

Yes 是

No 否