附件 二   船舶接獲高頻數位選擇呼叫遇險警報作業流程

Actions by Ships Upon Reception of HF DSC Distress Alert

# Text boxes

HF DSC distress alert

is received

接獲高頻DSC遇險呼叫警報

Listen on associated RTF or NBDP channel(s) for 5 min

於相關之無線電話或窄頻帶直接印字電報頻道上守聽5分鐘

Is the alert acknowled-ged or relayed by CS and/or RCC?

該警報是否被海岸電臺及/或搜救協調中心所確認或中繼?

Transmit distress relay on HF to coast station  and inform RCC

使用高頻發送遇險中繼至海岸電台並通知搜救協調中心

Is distress communicat-ion in progress on associated RTF channels?

相關無線電話頻率之遇險通信是否仍在進行?

Contact RCC VIA most efficient medium to offer assistance

透過有效之傳播媒介與搜救協調中心聯繫以提供協助

Enter details in log  詳情記錄於日誌簿

Reset system

系統重新設定

Is own vessel able to assist?

本船能否提供協助?

Yes 是

No 否

Remarks備註：

1. If it is clear the ship or persons in distress are not in the vicinity and/or other crafts are better placed to assist, superfluous communications which could interfere with search and rescue activities are to be avoided. Details should be recorded in the appropriate logbook.

如果清楚知道遇險船舶或人員不在附近及/或其他船艇更適合前往協助，應避免不必要之通信以干擾搜救行動，該詳情應紀錄於適當日誌簿上。

2. The ship should establish communications with the station controlling the distress as directed and render such assistance as required and appropriate.

船舶應依指示與控制遇險之電臺建立通信，使援助適當地符合需求。

3. Distress relay calls should be initiated manually.

遇險中繼呼叫應以人工啟動。

4. CS=Coast Station   RCC=Rescue Co-ordination Center

CS係指海岸電臺  RCC係指搜救協調中心

Yes 是

No 否

| HF DSC RTF and NBDP channels(kHz) 高頻數位選擇呼叫、無線電話及 窄頻帶直接印字電報之頻道 |
| --- |
| DSC | RTF | NBDP |
| 4207.5 | 4125 | 4177.5 |
| 6312.0 | 6215 | 6268 |
| 8414.5 | 8291 | 8376.5 |
| 12577.0 | 12290 | 12520 |
| 16804.5 | 16420 | 16695 |

Yes 是

No 否