圖一 船舶無線電臺審驗作業流程圖

| 國家通訊傳播委員會 北、中、南區監理處 | 申 請 者 （亦得委託辦理申請） |
| --- | --- |

備註：

1.依船舶無線電臺管理辦法第十九條第一項規定，船舶申請設置27MHz頻帶船舶用無線電對講機（DSB），免予申請架設許可證，經審驗合格後，核發船舶無線電臺執照。

2.依船舶無線電臺管理辦法第二十一條第二項規定，僅設置船舶用無線電對講機並取得專用執照者，其執照屆滿免經審驗得逕予換發新照；惟另裝設其他船舶無線電信設備，仍應經審驗合格後換發新照。

3.已於國外架設並經主管機關委託或認可之機構完成審驗者，直接申請船舶無線電臺執照時，審核人員應審核該審驗機構之審驗報告內容是否與原申請記載事項相符。

附表一   中華民國國家通訊傳播委員會

船舶電臺審驗登記表

| 1.船舶名稱： | 2.電臺呼號： |
| --- | --- |
| 3.MMSI號碼： | 4.船舶號數(或小船編號)： |
| 5.船舶所有人： | 6.船舶種類： |
| 7.船籍港： | 8.航行海域： |
| 9.電臺種類： | 10.公眾通信種類： |
| 11.電臺執照：有效日期 / / | 12.換照期限(年)： |
| 13.漁船統一編號： | 14.總噸數： |

15.設備：

（一）主要設備：

| 機件名稱 | 廠 牌 | 型 號 | 數量 | 發射類別 | 頻帶或指配頻率 | 功 率 | 機件狀態 | 備 註 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

（二）備用設備：

| 機件名稱 | 廠 牌 | 型 號 | 數量 | 發射類別 | 頻帶或指配頻率 | 功 率 | 機件狀態 | 備 註 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

附表一

（三）其他設備：

| 機件名稱 | 廠 牌 | 型 號 | 數量 | 發射類別 | 頻帶或指配頻率 | 功 率 | 機件狀態 | 備 註 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

16.設備更新、異動記載 (初次審驗不用填)

| (*) 項目 | 設備名稱 | 審驗人員 | 審驗地點 | 日期 |
| --- | --- | --- | --- | --- |
|  | 廠牌 | 型式 | 簽發認證單位 | 位置 |  |  |  |
|  | 備註： |  |  |  |
|  | 舊機件流向： |  |  |  |

(*) 本欄必須與報告項目相符

備註：

1.本表可由本會電腦TRAIS系統直接印出，供審驗人員審核、加註。

2.審核之相關證明文件種類如下（參考用）：

申請人（船舶所有人）部分：身分證明文件、公司證明文件或營利事業登記證影本......等。

船舶登記證明文件部分：船舶登記證影本、小船執照影本；非小船為船舶檢查證書影本及（臨時）國籍證書影本或（娛樂）漁船之（娛樂）漁業執照......等。

附表一

附表二  中華民國國家通訊傳播委員會

非全球海上遇險及安全系統船舶無線電臺審驗報告

審驗報告編號：

審驗日期 ：       /     /                               審驗地點：

一、基本資料

| 1 | 船名： | 2 | 電臺呼號： |
| --- | --- | --- | --- |
| 3 | MMSI號碼： | 4 | 船舶號數(或小船編號)： |
| 5 | 船籍港： | 6 | 船舶種類： |
| 7 | 總噸數： | 8 | 電臺種類： |
| 9 | 航行海域： | 10 | 漁船統一編號： |
| 11 | 公眾通信種類： | 12 | 換照期限： |
| 13 | 船舶所有人： 聯絡 電話： 地 址： |

（請將審驗結果於□中填入×，若無該項設備時填入N.A.）

二、一般審驗                                                               是 否

| 1.電臺設備放置是否適當、天線是否固定牢靠.................................. | □□ |
| --- | --- |
| 2.是否設有緊急照明燈、準確時鐘................................... | □□ |
| 3.是否有備用電源□充電設備或□備用發電機............................. | □□ |
| 3.1 安全燈及特高頻或(及)中/高頻無線電設備，切換至備用電源是否正常操作... 3.2 備用電源之電壓 DC V ；或比重計測得其比重 | □□ |
| 3.3 主要電源電壓 AC V |  |
| 4.是否有下列參考文件： |  |
| 4.1無線電日誌簿........................................................ | □□ |
| 4.2經常收受通信之海岸/漁業通信電臺表.................................. | □□ |
| 4.3是否備有水上行動業務相關手冊【國際航線（漁船免備）：ITU發行之水上行動業務實用手冊與相關文件；國內航線及所有漁船：船舶無線電臺通信作業要點。】.............................................................. | □□ |
| 5.是否有□備用天線（國內航線或經濟海域內者免備）或□備用發射機............. | □□ |

三、設備測試

1. 中/高頻（M/HF）無線電設備 （若有裝設）                                    是 否

| 1.1收發話機是否具備開關或按扭，能於緊急時立即使用2182kHz呼救頻率 ....... | □□ |
| --- | --- |
| 1.2各發送頻率是否皆已預為調妥，而能快速變換............................... | □□ |
| 1.3發話機輸出電功率是否超過400W(PEP).................................... | □□ |
| 1.4若另裝設中/高頻數位選擇呼叫接收、發射設備者，其數位選擇呼叫號碼是否燒錄正確.................................................................. | □□ |
| 1.5若另裝設中/高頻數位選擇呼叫守聽接收設備者，能否產生清晰警報聲響........ | □□ |

附表二

1.6 中/高頻（M/HF）無線電話之主要設備功率及頻率容許差度測試

| Carrier Frequency （MHz） | Assigned Frequency （MHz） | Class of Emission | Radiated Power (W)(PEP) | Measured Carrier Frequency(MHz) | Frequency Tolerances(Hz) | Tolerances Standard(Hz) |
| --- | --- | --- | --- | --- | --- | --- |
| 2.182 | 2.1834 | J/H3E |  |  |  | (40Hz |
| 8.255 | 8.2564 | J3E |  |  |  | (50Hz |
| ＊以下頻率擇一測試 4.125 6.215 12.290 | 4.1264 6.2164 12.2914 | J3E |  |  |  |  |
| 27.065※ | 27.065 | A3E |  |  |  |  |

※ 27.065MHz為DSB警急遇險共同呼叫頻率亦應測試

1.7 中/高頻（M/HF）無線電話之備用設備功率及頻率容許差度測試（若有裝設）

| Frequency (MHz) | Assigned Frequency (MHz) | Class of Emission | Radiated Power (W)(PEP) | Measured Carrier Frequency(MHz) | Frequency Tolerances(Hz) | Tolerances Standard(Hz) |
| --- | --- | --- | --- | --- | --- | --- |
| 2.182 | 2.1834 | J/H3E |  |  |  | (40Hz |
| 8.255 | 8.2564 | J3E |  |  |  | (50Hz |
| ＊以下頻率擇一測試 4.125 6.215 12.290 | 4.1264 6.2164 12.2914 | J3E |  |  |  |  |

1.8 中/高頻（M/HF）無線電設備

| 廠 牌 | 型、序號 | 頻率範圍 |
| --- | --- | --- |

2.  特高頻（VHF）無線電設備（若有裝設）

| 待 測 頻 道 | 待 測 頻 率(MHz) | Radiated Power ((25W，並可降低至1W) | Measured Carrier Frequency(MHz) | Frequency Tolerances(Hz) | Tolerances Standard(Hz) |
| --- | --- | --- | --- | --- | --- |
| 13 | 156.65 |  |  |  | (10 PPM |
| 16 | 156.80 |  |  |  |  |
| 1* | 156.05 |  |  |  |  |
| 3* | 156.15 |  |  |  |  |
| 28* | 157.40 |  |  |  |  |

＊這些頻道可擇一測試                                                       是 否

2.1 與其他電臺或特高頻手持式雙向無線電話測試是否能正常通話.................□ □

2.2 若另裝設特高頻數位選擇呼叫接收、發射設備者，其數位選擇呼叫號碼是否燒錄正確

（若有裝設）.............................................................□ □

2.3特高頻（VHF）無線電設備

| 廠 牌 | 型、序號 | 頻率範圍 |
| --- | --- | --- |

附表二

3.  應急指位無線電示標（EPIRB）

|  | 廠 牌 | 型、序號 | 操作頻率 | 電池有效日期（月/日/年） |
| --- | --- | --- | --- | --- |
| P-side |  |  | 406~406.1MHz+121.5MHz |  |
| S-side |  |  | 406~406.1MHz+121.5MHz |  |

是  否

3.1 是否固定安置於駕駛艙外兩側明顯可及處並不影響自動浮離功能（衛星應急指位無線電示標應配合裝置於自動浮離裝置上）.....................................□ □

3.2 衛星應急指位無線電示標燒錄MMSI號碼是否正確............................□ □

3.3 應急指位無線電示標是否能正常操作，並有定期試驗及更換電池紀錄...........□ □

自動浮離裝置有效日期：       年      月     日

4.  航行警告電傳接收機（NAVTEX;若有裝設）                                  是 否

4.1航行警告電傳接收機自動測試功能是否正常.................................□ □

4.2檢視最近所接收之列印資訊是否正常.......................................□ □

| 廠 牌 | 型、序號 | 樣式 |
| --- | --- | --- |
|  |  | □國際頻率518kHz □國內區域性頻率 |

5. 搜救定位裝置【雷達詢答機(SART)或AIS搜救發送器(AIS-SART);若有裝設】     是 否

5.1配合船上9 GHz雷達或AIS，產生定位信號是否正常（若有裝置）. . .. ..□ □

5.2安裝位置及固定方式是否適當.............................................□ □

| 廠 牌 | 型、序號 | 電池有效日期 |
| --- | --- | --- |
|  |  | 年 月 日 |
|  |  | 年 月 日 |

6. 手持式雙向特高頻無線電話                                     是 否

6.1與其他電臺或特高頻手持式雙向無線電話測試是否能正常通話.................□ □

6.2若採用充電電池，船上應有充電設施；若採用原電池（一次使用）應於電池有效日期期限內..................................................................□ □

7.其他設備：

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

________________________________________________________________________________

附表二

8.設備更新、異動記載 (初次審驗不用填)

| (*) 項目 | 設備名稱 | 審驗人員 | 審驗地點 | 日期 |
| --- | --- | --- | --- | --- |
|  | 廠牌 | 型式 | 簽發認證單位 | 位置 |  |  |  |
|  | 備註： |  |  |  |
|  | 舊機件流向： |  |  |  |

四、審驗意見：

________________________________________________________________________________

________________________________________________________________________________

________________________________________________________________________________

________________________________________________________________________________

□ 國家通訊傳播委員會 北/中/南區監理處

□ 經主管機關委託或認可之機構

公司行號：

公司印章：                                     審驗人                  簽章

年        月       日

報告審核人：

□ 基本資料是否相符。

□ 申請記載事項與原船舶無線電臺執照、架設許可或專案核准內容等，是否相符。

附表二

附表三  中華民國國家通訊傳播委員會

非全球海上遇險及安全系統之船舶用無線電對講機審驗表

中華民國      年     月    日

一、27MHz船舶用無線電對講機

| 船 舶 資 料 | 船 名 |  |
| --- | --- | --- |
|  | 船舶所有人 |  |
|  | 船舶號數（或小船編號、漁船統一編號） |  |
|  | 所 屬 區 漁 會 或 船 籍 港 |  |
| 證照記 錄事項 | 執照字號及日期 |  |
|  | 異 動 記 錄 |  |
| 對 講 機 廠 牌 及 型 式 |  |
| 發 射 機 部 分 | 實測功率 |  |
|  | 規 定 頻 率 | 27.065MHz | 實測頻率 (容許差度) 50 PPM |  |
|  | ※ 90%＜最大調幅度＜100% |  |
| ※ 接收機 部分 | 總諧波失真率＜10% |  |
|  | 音頻功率＞2W |  |
|  | 靈敏度＜2μV |  |
| 審 驗 編 號 |  |
| 審驗結果 | 合 格 |  |
|  | 不合格 |  |
| 備註 |  |

※如因場地、器材或時間因素限制時，可選擇性測試。

二、登船審驗時，一般審驗項目或有增設其他船舶電信設備，仍應配合附表二非全球海上遇險及安全系統船舶無線電臺審驗報告相關項目辦理審驗。

□ 國家通訊傳播委員會 北/中/南區監理處

□ 經主管機關委託或認可之機構

公司行號：

公司印章：                                     審驗人                  簽章

年        月       日

報告審核人：

□ 基本資料是否相符。

□ 申請記載事項與原船舶無線電臺執照、申請書或專案核准文件內容等，是否相符。

附表三

附表四

中華民國國家通訊傳播委員會

全球海上遇險及安全系統船舶無線電臺審驗報告

NATIONAL COMMUNICATIONS COMMISSION

REPUBLIC OF CHINA

Survey Report of Ship Radio Installations

(  GMDSS  )

Two Parts are included

I.Check List for the Report of Ship Radio Installations

II. RECORD OF SHIP SAFETY RADIO

附表四

附表四-I

中華民國國家通訊傳播委員會

船舶安全無線電設備審驗表

(GMDSS設備)

NATIONAL COMMUNICATIONS COMMISSION

REPUBLIC OF CHINA

Check List for the Report of Ship Radio Installations

(GMDSS)

| □初次審驗 | □換證審驗 | □年度審驗 | □額外審驗 |
| --- | --- | --- | --- |

| Report No | Date issued | Issued at |  |
| --- | --- | --- | --- |
| Name of ship | IMO No | Call Sign | MMSI |
| Ship number | Port of Registry | Keel Laid | Gross Tonnage |
| Ship Owner and Address |
| Place of Survery □In drydock □On slipway □Afloat | Survery commenced Mm/dd/year | Survery completed Mm/dd/year |

Conclusion

Suveryor

Note: Fill out the blanks and check with “X” as appropriate in (

附表四-I

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Check list for the survey of Ship Radio Installations

1.	Basic Data

1.1	Ship navigating sea areas (Reg. IV/2, 8, 9, 10, 11)

A1	A1+A2 	A1+A2+A3  A1+A2+A3+A4

1.2	Methods of ensuring availability of Equipment (Reg. IV/15)

Duplication of equipment  shore based maintenance  At-sea electronic maintenance capacity

1.3	Actual Provision of ship‘s radio equipment

VHF	MF	MF/HF	INMARSAT	B/C/F77

Primary System:

Duplicated System:

2.	General	          InS/PS/RS*

2.1	Confirming that any new equipment has been properly approved before installation and that no changes have been made such as would affect the validity of the certificate......................................................................................[]

2.2	Radio records kept in the period since the last survey to the satisfaction of the Administration and as required by the Radio Regulations (Reg. IV/17).........................................................................................................................[]

2.3	Checking documentary evidence that the actual capacity of the battery has been proved in port within the last 12 months (Reg. IV/13)...........................................................................................................................................................................[]

2.4	Confirming that all Radio equipment complies with appropriate performance standards not inferior to those adopted by IMO (Reg. IV/14)......................................................................................................................................[]

3.	Examination of radio installations

3.1	Examining the position, physical and electromagnetic protection and illumination of each radio installation (Reg. IV/6)...................................................................................................................................................................[]

3.2	Confirming the provision of equipment for the radio installation with due regard to the declared sea areas in which the ship will trade and the declared means of maintaining availability of functional requirements (Reg. III/6, IV/7 to 11, 14 and 15)..............................................................................................................................................................................[]

3.3	Confirming the ability to initiate the transmission of ship-to-shore distress alerts by at least two separate and independent means, each using a different radiocommunication service, from the position from which the ship is normally navigated (Reg. IV/4, 7 to 11).......................................................................................................................[]

3.3.1   Secondary means of alerting

VHF(DSC) INMARSAT-B/-F77 INMARSAT-C MF(DSC) HF(DSC) VHF EPIRB
406MHz EPIRB (close to, or by remote activation from bridge)

3.4	Checking that the following ship‘s radio equipment operates from the main, emergency (if provided) and reserve sources of energy (Reg. IV/13)......................................................................................................................[]

VHF	MF	MF/HF	INMARSAT  B/CF77

Primary System:

Duplicated System:

3.5	Antennas

3.5.1	Visually checking all antennas, including INMARSAT antennas, and feeders for satisfactory sitting and absence of defects (Reg. IV/14).................................................................................................................................[]

3.5.2	Checking insulation and safety of all antennas..............................................................................................[]

3.6	Reserve source of energy

3.6.1	Checking there is sufficient capacity to operate the basic or duplicated equipment for 1 hour(with emergency sources) or 6 hours(without emergency sources), as appropriate (Reg. IV/13).........................................................[]

3.6.2	And, if the reserve source of energy is a battery:

3.6.2.1	Checking its sitting and installation(Reg. IV/13).............................................................................................[]

3.6.2.2	Where appropriate, checking its condition by specific gravity measurement or voltage

measurement －specific gravity =           or voltage =           volts..........................................................[]

3.6.2.3	With the battery off charge, and the maximum required radio installation load connected to the reserve source of energy, checking the battery voltage and discharge current................................................................[]

3.6.2.4	Checking that the charger(s) are capable of recharging the reserve battery within 10 hours (Reg. IV/13)................................[]

Page         of

附表四-I

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Check list for the survey of Ship Radio Installations

Survey condition code as follows:

| 0 : | Not applicable | 2 : | Satisfactory after treatment, see further reports in head page/ Memoranda |
| --- | --- | --- | --- |
| 1 : | Satisfactory | 3 : | Outstanding recommendation/ Surveyor’s note, see further reports in head page/ Memoranda |
| Note: Entries in boxes□shall be made by inserting a cross (x) as appropriate. |

3.7	VHF transceiver(s), Primary Duplicated

3.7.1	Checking for operation on channels 6,13 and 16 (Reg. IV/7 and 14)...........................................................[]

3.7.2	Checking for correct operation of all controls, including priority of control units (Reg. IV/14).......................[]

3.7.3	Checking the operation of the VHF control unit(s) or portable VHF transceiver provided for navigational safety from the wing of bridge (Reg. IV/6)............................................................................................................................[]

3.7.4	Checking for correct operation by on-air contact with a coast station or other ship..........................[]

3.8.	VHF DSC, Primary Duplicated

3.8.1	Confirming that the correct selective calling number is programmed in the equipment................................[]

3.8.2	Checking the off-air self-test programme......................................................................................................[]

3.8.3	Checking for correct transmission by means of a routine or test call to a coast station,

other ship, on-board duplicate equipment or special test equipment...........................................[]

3.9	CH70 DSC watch receiver, Primary Duplicated

3.9.1	Checking for correct reception by means of a routine or test call from coast station,

other ship, on-board duplicate equipment or special test equipment...........................................[]

3.9.2	Checking that a continuous watch is being maintained whilst operating VHF transceiver............................[]

3.9.3	Checking the audibility of the VHF/DSC alarm..............................................................................................[]

3.10	MF radiotelephone equipment (Primary)

3.10.1	Checking the antenna tuning in all appropriate bands..................................................................................[]

3.10.2	Checking for correct operation by contact with a coast station and / or measuring

transmission line quality and radio frequency output..............................................................................[]

3.10.3	Checking receiver performance by monitoring known stations on all appropriate bands.............................................................[]

3.10.4	If control units are provided outside the navigating bridge, checking the control unit on the bridge has first priority for the purpose of initiating distress alerts (Reg. IV/9, 10, and 14)................................................................[]

3.11	MF DSC controller(s) (Primary)

3.11.1	Confirming that the correct Maritime Mobile Service Identity is programmed in the equipment..................................................[]

3.11.2	Checking the off-air self-test programme......................................................................................................[]

3.11.3	Checking operation by means of a test call on MF to a coast radio station if the rules of the berth permit the use of MF transmissions (Reg. IV/9, 10 )...................................................................................................................[]

3.12	MF DSC watch receiver(s) (Primary)

3.12.1	Checking that a continuous watch is being maintained whilst operating MF radio transceivers (Reg. IV/12).................[]

3.12.2	Checking for correct operation by means of a test call from a coast station or other ship..................[]

3.12.3	Checking the audibility of the MF DSC alarm............................................................................................[]

3.13	MF/HF radiotelephone equipment, Primary Duplicated

3.13.1	Checking the antenna tuning in all appropriate bands....................................................................................[]

3.13.2	Checking for correct operation by contact with a coast station and / or measuring

transmission line quality and radio frequency output.................................................................................[]

3.13.3	Checking receiver performance by monitoring known stations on all appropriate bands................................[]

Page         of

附表四-I

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Check list for the survey of Ship Radio Installations

3.13.4	If control units are provided outside the navigating bridge, checking the control unit on the bridge has first priority for the purpose of initiating distress alerts (Reg. IV/9, 10, and 14)...................................................................[]

3.14	MF/HF radiotelex equipment, Primary Duplicated

3.14.1	Confirming that the correct selective calling number is programmed in the equipment...............................................................[]

3.14.2	Checking correct operation by inspection of recent hard copy or by a test with a coast  radio Station (Reg. IV/10

and 11).....................................................................................................................................................[]

3.15	MF/HF DSC controller(s), Primary Duplicated

3.15.1	Confirming that the correct Maritime Mobile Service Identity is programmed in the equipment......................[]

3.15.2	Checking the off-air self-test programme........................................................................................................[]

3.15.3	Checking operation by means of a test call on MF and HF to a coast radio station if the rules of the berth permit the use of MF/HF transmissions (Reg. IV/9, 10 )..............................................................................................[]

3.16	MF/HF DSC watch receiver(s), Primary Duplicated

3.16.1	Checking that a continuous watch is being maintained whilst operating MF/HF radio transceivers (Reg. IV/12)...........................................................................................................................................................................[]

3.16.2	Checking for correct operation by means of a test call from a coast station or other ship.................[]

3.16.3	Checking the audibility of the MF/HF DSC alarm..........................................................................................[]

3.17	INMARSAT - B, C or F77  ship earth station(s), Primary Duplicated

3.17.1	Checking that the correct INMARSAT Identity is programmed in the equipment...........................................[]

3.17.2	Checking that the equipment operates from the main, emergency (if provided) and reserve sources of energy, and that where an uninterrupted supply of information from the ship‘s navigational or other equipment is required ensuring such information remains available in the event of failure of the ship’s main or emergency source of electrical power (Reg. IV/13 and 14)..........................................................................................................................................[]

3.17.3	Checking the distress function by means of an approved test procedure where possible (Reg. IV/10, 12 and 14)...............................................................................................................................................................................[]

3.17.4	Checking for correct operation by inspection of recent hard copy or  by test call..............................[]

3.18	NAVTEX equipment (Reg. IV/7, 12 and 14)

3.18.1	Checking for correct operation by monitoring incoming messages or inspecting recent hard copy.................................[]

3.18.2	Running the self-test programme if provided..................................................................................................[]

3.19	Enhanced group call equipment, if provided (Reg. IV/7 and 14)

3.19.1	Checking for correct operation and area by monitoring incoming messages or by inspecting recent hard copy.........................[]

3.19.2	Running the self-test programme if provided..................................................................................................[]

3.20	Radio equipment for receipt of maritime safety information by HF NBDP; if provided (Reg. IV/7, 12 and 14)

3.20.1	Checking for correct operation by monitoring incoming messages or inspecting recent hard copy...[]

3.20.2	Running the self-test programme if provided..................................................................................................[]

3.21	EPIRB, 406MHz 1.6GHz CH 70 EPIRB (Reg. IV/7 and 14)

3.21.1	Checking position and mounting for float-free operation................................................................................[]

3.21.2	Carrying out visual inspection for defects.......................................................................................................[]

3.21.3	Carrying out the self-test routine.....................................................................................................................[]

3.21.4	Checking that the EPIRB Identity is clearly marked on the outside of the equipment and decoding the EPIRB identity number and confirming it is correct.................................................................................................................[]

3.21.5	Checking the battery expiry date:               (D/M/Y)............................................................................................[]

3.21.6	If provided, checking the hydrostatic release and its expiry date:               (D/M/Y).....................................................[]

3.22	Two-way VHF radiotelephone apparatus (Reg. III/6)

3.22.1	Checking for correct operation on channel 16 and one other by testing with another fixed orportable VHF installation(Reg.IV/14).........................................................................................................................................[]

3.22.2	Checking the battery charging arrangements, where rechargeable batteries are used (Reg.IV/14)...............[]

3.22.3	Checking the expiry date of primary batteries, where used (Reg. IV/14)

No.1                    No.2                    No.3                    (D/M/Y)................[]

3.22.4	Where appropriate, checking any fixed installation provided in a survival craft (Reg. IV/14)..........................[]

3.23	Search and rescue locating devices (Radar transponder/AIS-SART) (Reg. III/6, IV/7 and 14)

3.23.1	Checking the position and mounting................................................................................................................[]

3.23.2	Monitoring response on ship‘s 9 GHz radar /AIS................................................................................................................[]

3.23.3	Checking the battery expiry date:  No.1                 No.2               	(D/M/Y)	.............................[]

3.24	Examining the test equipment and spares carried to ensure carriage is adequate in accordance with the sea areas in which the ship trades and the declared options for maintaining availability of the functional requirements (Reg. IV/15)..............................[]

Page         of

附表四-I

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Check list for the survey of Ship Radio Installations

4	Documentation

4.1	A valid radio license issued by the flag Administration (ITU RR Art. 24).......................................................[]

4.2   ※	Radio operator‘s certificates of competence (Reg. IV/16, ITU RR Art. 56, Chapter VIII / STCW).............................................[]

| * | Name of Radio Operator | Class & Certificate No. | Certificate issued by |
| --- | --- | --- | --- |

* Entry in the box shall be made by inserting a cross (x) mark for the radio operator who is designated to have primary responsibility for radiocommunications during incidents.

4.3	Radio record (log) for GMDSS (Reg. IV/17 and ITU RR App. 11)...........................................................[]

4.4	Carriage of up-to-date ITU publications (ITU RR App. 11).......................................................................[]

4.5	Carriage of operating manuals for all equipment (Reg. IV/15).................................................................[]

4.6	Carriage of service manuals for all equipment when at-sea maintenance is the declared option (Reg. IV/15).........................................................................................................................................................................[]

5.     Equipment renewal, alteration and/ or addition ( for Chinese Flag only )

5.1    All  safety radiotelegraph installations /  safety radiotelephone installations were disconnected from electric power

along with antenna but their equipment are still kept on board....................................................................................................[]

5.2    Equipment as mentioned in Ship Station License No                      issued by NATIONAL COMMUNICATIONS COMMISSION was checked and found :

Not altered

Altered.  List  the equipments which has been altered in the following spaces

| Equipment | Equipment(Newly installed on board) (Model and Quantity) | Equipment listed in the Ship Station License (Model and Quantity) |
| --- | --- | --- |
| Primary |  |  |
| Duplicated |  |  |
| Others |  |  |

6.	Survey Results

The above survey items have been checked and found in compliance with relevant provisions of convention.

7.	Memoranda

Survey's Note

Outstanding Recommendation

The record of safety radio installation is updated if the equipment has been altered.

Page         of

※：This item is not required.

附表四-I

附表四-II

中華民國國家通訊傳播委員會

船舶安全無線電設備記錄

(GMDSS設備)

NATIONAL COMMUNICATIONS COMMISSION

REPUBLIC OF CHINA

RECORD OF SHIP SAFETY RADIO

(GMDSS)

To meet the provisions of the SOLAS 1974 as amended in 1988 for the GMDSS,the form must be kept on board and be available for inspection by a nominated surveyor or recognized organization at all times.

| Report No. | Date issued | Issued at |
| --- | --- | --- |
| Name of ship | IMO No. | Ship number |
| Port of Registry | Keel Laid | Gross Tonnage |
| Place of Survey (in drydock ( on slipway (afloat | Survey commenced (mm/dd/year) | Survey completed (mm/dd/year) |
| Call Sign: ID for DSC((MF/(MF/HF): ID for INMARSAT-C: 1st ID for INMARSAT-B: ID for INMARSAT-F77 | ID for DSC(VHF): ID for NBDP: ID for Satellite EPIRB: 2nd ID for INMARSAT-B: |

Navigating Sea Areas: (A1 (A1+A2 (A1+A2+A3 (A1+A2+A3+A4

Maintenance Requirements: (Duplication of Equipment (Shore-based Maintenance (At Sea Maintenance

Note: Fill out the blanks and check with “×” as appropriate in (

附表四-II

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Record of Ship Safety Radio

1.	Source of electrical power

1.1	Main Source of energy [Reg. IV/13.1]

|  | VAC × |  | kVA × |  | Set(s) |
| --- | --- | --- | --- | --- | --- |

1.2	Emergency Source of electrical power [Reg. II-1/42, 43]

1.2.1	 Emergency generator

|  | VAC × |  | kVA × |  | Set(s) , Located |  | , or |
| --- | --- | --- | --- | --- | --- | --- | --- |

1.2.2	 Accumulator batteries

|  | VDC × |  | Ah × |  | Set(s) , Located |  |
| --- | --- | --- | --- | --- | --- | --- |

1.2.3	Equipment’s operated by emergency source of electrical power for 18 hours or more.

VHF radio installation of  primary /  Duplicated system with DSC watch receiver............................................[]

MF radio installation with DSC watch receiver...........................................................................................................[]

MF/ HF radio installation of  Primary /  Duplicated system with DSC watch receiver.......................................[]

INMARSAT SES of  Primary /  Duplicated system............................................................................................[]

1.3	Reserve source of energy (battery) [Reg. IV/ I3]

| Manufacturer | Type | Voltage | Capacity | Specific Gravity of Acid | Located at |
| --- | --- | --- | --- | --- | --- |

1.3.1 	Type and maker of means of automatically charging................................................................................................................[]

1.3.2    Equipment operated by reserve source of energy for  1 /  6 hours or more.

Emergency light for radio controller............................................................................................................................[]

VHF radio installation of  Primary /  Duplicated system....................................................................................[]

MF radio installation for Primary system.....................................................................................................................[]

MF/ HF radio installation of  Primary /  Duplicated system................................................................................[]

INMARSAT SES of  Primary /  Duplicated system............................................................................................[]

2.	Radio life-saving appliances [Reg. III/6.2]

2.1	Two-way VHF radiotelephone apparatus

| No. | Manufacturer | Type (Serial No.) | Channels | Approved by | Locate at |
| --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |

2.2	Search and rescue locating devices (Radar transponder/AIS-SART)

| No. | Manufacturer | Type (Serial No.) | Channels | Approved by | Located at |
| --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |

3.	Radio installation [Reg. IV/6]

3.1	Location and environmental conditions of radio installation.......................................................................[]

3.2	Emergency light for radio controller............................................................................................................[]

3.3	Clearly marking of call sign, ship’s ID and other codes..............................................................................[]

Page         of

附表四-II

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Record of Ship Safety Radio

4.	Composition of radio installation [Reg. IV/8, 9, 10, 11 & 15]

4.1	Primary system

| VHF.... | , MF... | , MF/ HF..... | , INMARSAT..... /B/C/F77 |
| --- | --- | --- | --- |

4.2 	Duplicated system

| VHF..... | , | MF/ HF | , INMARSAT /B/C/F77 |
| --- | --- | --- | --- |

4.3 	Second means of alerting

| INMARSAT..... /B/C/F77 | , VHF EPIRB..... | , INMARSAT EPIRB |
| --- | --- | --- |
| 406MHz EPIRB..... | , VHF DSC..... | , MF DSC..... | , MF/HF DSC |

5.	Primary system(P) & duplicated system(D) [Reg. IV/7, 8, 9, 10 & 11]

5.1	VHF radio installation

|  | Manufacturer | Type (Serial No.) | Channels | Approved by |
| --- | --- | --- | --- | --- |
| P |  |  |  |  |
| D |  |  |  |  |

5.1.1 	Initiation of DSC distress alert on CH 70 from normal navigating position.............................................................[]

5.1.2	Highest priority of controller in wheel house............................................................................................................[]

5.1.3 	Facilities of bridge wings communication.

| Extension cords................ | , Fixed handset line............ | , Portable VHF transceiver............... |
| --- | --- | --- |

5.1.4 	VHF DSC

Combined with VHF radio installation..........................................................................................................................[]

Separated from VHF radio installation..........................................................................................................................[]

－Separated VHF DSC

|  | Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- | --- |
| P |  |  |  |  |
| D |  |  |  |  |

5.1.5 	VHF DSC watch receiver :

Combined with VHF radio installation.........................................................................................................................[]

Separated from VHF radio installation.........................................................................................................................[]

－Separated VHF DSC watch receiver on CH 70

|  | Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- | --- |
| P |  |  |  |  |
| D |  |  |  |  |

5.1.6 	Printer, if provided

|  | Manufacturer | Type (Serial No.) |
| --- | --- | --- |
| P |  |  |
| D |  |  |

5.2 	MF radio installation

| Manufacturer | Type (Serial No.) | Frequency range | Approved by | Located at |
| --- | --- | --- | --- | --- |

5.2.1 	Initiation of DSC distress alert on 2187.5 kHz from navigating position..................................................................[]

5.2.2 	MF DSC

Combined with MF radio installation............................................................................................................................[]

Separated from MF radio installation.............................................................................................................................[]

－Separated DSC installation

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

Page         of

附表四-II

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Record of Ship Safety Radio

5.2.3 	MF DSC watch receiver

Combined with MF radio installation................................................................................................................................[]

Separated from MF radio installation................................................................................................................................[]

－Separated DSC watch receiver on 2187.5 kHz.

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

5.2.4 	Printer, if provided.

| Manufacturer | Type (Serial No.) |
| --- | --- |

5.3 	MF/ HF radio installation.

|  | Manufacturer | Type (Serial No.) | Type of battery | Approved by | Located at |
| --- | --- | --- | --- | --- | --- |
| P |  |  |  |  |  |
| D |  |  |  |  |  |

5.3.1 	Initiation of DSC distress alert from normal navigating position.

| 2187.5 kHz | 4207.5 kHz | 6312 kHz | 8414.5 kHz | 12577 kHz | 16804.5 kHz.................[] |
| --- | --- | --- | --- | --- | --- |

5.3.2	DSC distress alert watch frequencies in normal navigating position.

| 2187.5 kHz | 4207.5 kHz | 6312 kHz | 8414.5 kHz | 12577 kHz | 16804.5 kHz.................[] |
| --- | --- | --- | --- | --- | --- |

5.3.3 	MF/ HF DSC

Combined with MF/ HF radio installation......................................................................................................................[]

Separated from MF/ HF radio installation......................................................................................................................[]

－Separated MF/ HF DSC installation

|  | Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- | --- |
| P |  |  |  |  |
| D |  |  |  |  |

5.3.4 	MF/ HF DSC watch receiver

Combined with MF/ HF radio installation.....................................................................................................................[]

Separated from MF/ HF radio installation.....................................................................................................................[]

－Separated MF/ HF DSC watch receiver

|  | Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- | --- |
| P |  |  |  |  |
| D |  |  |  |  |

5.3.5 	Direct printing telegraphy

Combined with MF/ HF radio installation......................................................................................................................[]

Separated from MF/ HF radio installation......................................................................................................................[]

－Separated direct printing telegraphy installation

|  | Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- | --- |
| P |  |  |  |  |
| D |  |  |  |  |

5.3.6 	Printer, if provided.

|  | Manufacturer | Type (Serial No.) |
| --- | --- | --- |
| P |  |  |
| D |  |  |

Page         of

附表四-II

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Record of Ship Safety Radio

6.	INMARSAT ship earth station. [Reg. IV/10 & 11]

|  | INMARSAT | Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- | --- | --- |
|  | B C F77 |  |  |  |  |
| P |  |  |  |  |  |
| D |  |  |  |  |  |

6.1 	Initiation of distress alert from normal navigation position.......................................................................................[]

6.2 	Antenna situation........................................................................................................................................................[]

as high as possible.......................................................................................................................................................[]

in such a position that no obstacles to significantly degrade the performance...........................................................[]

6.3 	In case of INMARSAT B, INMARSAT F77 or other tracking antenna..................................................................[]

Continuous supply of ship’s heading information

7.	MSI receiving facilities [Reg. IV/7 & 12]

7.1 	NAVTEX receiver

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

7.2 	EGC receiver/ decoder

built in INMARSAT-C................................................................................................................................................[]

added to INMARSAT-B…………………..................................................................................................................[]

added to INMARSAT-F77………………..................................................................................................................[]

separated from INMARSAT SES................................................................................................................................[]

－Separated/ added type of EGC receiver or decoder

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

7.3 	HF NBDP receiver

built in MF/ HF radio installation..................................................................................................................................[]

separated from MF/ HF..................................................................................................................................................[]

－Separated HF NBDP receiver

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

8.	EPIRB [Reg. IV/6.4, 7]

8.1 	VHF EPIRB (In case of ship navigating only in A1 Area)........................................................................................[]

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

8.2 	Satellite EPIRB

COSPAS-SARSAT system (406 MHz)..........................................................................................................................[]

INMARSAT system (1.6 GHz)......................................................................................................................................[]

|  | Manufacturer | Type (Serial No.) | Approved by | Located at | Homing Freq. |
| --- | --- | --- | --- | --- | --- |
| No. 1 |  |  |  |  |  |
| No. 2 |  |  |  |  |  |

8.3 	Float-free release and activation arrangements

|  | Manufacturer | Type (Serial No.) | Approved by |
| --- | --- | --- | --- |
| No. 1 |  |  |  |
| No. 2 |  |  |  |

9.	Search and rescue locating devices [Reg. IV/7]

9.1 	One of those required by Reg. III/ 6.2.2 for survival craft........................................................................................[]

9.2 	Use exclusively on board ship...................................................................................................................................[]

Search and rescue locating devices (Radar transponder/AIS-SART) used exclusively.

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

Page         of

附表四-II

NATIONAL COMMUNICATIONS COMMISSION REPUBLIC OF CHINA

Record of Ship Safety Radio

10.	Radiotelephone distress frequency facilities on 2182 kHz [Reg. IV/7]

10.1 	Radiotelephone distress frequency watch receiver

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

10.2 	Radiotelephone alarm signal generator

| Manufacturer | Type (Serial No.) | Approved by | Located at |
| --- | --- | --- | --- |

11.	Position updating

| Automatically provided by GPS, GLONASS, |  | [] |
| --- | --- | --- |
| Manually updated |  | ..................................................................................................................[] |

12.	Documents [Reg. IV/17 & Appendix 11 Sec. VA of ITU Radio Regulation)

12.1 	Radio Station License.......................................................................................................................................[]

12.2 ※	Certificates of radio personnel..........................................................................................................................[]

12.2 	Radio log...........................................................................................................................................................[]

12.3 	List of coast station...........................................................................................................................................[]

12.4 	List of ship station.............................................................................................................................................[]

12.5 	Manual for use by maritime mobile and maritime mobile-satellite service......................................................[]

13.	Other equipment where provided

| Item | Manufacturer | Type |
| --- | --- | --- |

14.	Particular of any special features or additional information

| Item number (*) | DESCRIPTION |
| --- | --- |

15.	Equipment renewals, alterations and/or additions effected since the record was prepared.

| Item number (*) | DESCRIPTION | Surveyor | Port | Date |
| --- | --- | --- | --- | --- |

| Port |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Date |  |  | Surveyor |  |  | Technician |  |
|  |  |  |  | ( |  | ) |  |  | ( |  | ) |

Page         of

- ：This item is not required.

附表四-II

（參考範例）

# Text boxes

收件：

僅限申請複驗一次

印章

印章

□合格   □不合格

備註：審驗不合格者，應於  年  月  日前申請複驗，並以一次為限。

以下為受理單位填寫

船舶無線電臺審驗申請書 □書面 □傳真

年     月      日    時    分

本（船舶所有人）為   （船名）  船舶，申請     字第          號

□新設船舶無線電臺／□船舶用無線電對講機（娛樂漁業漁船）

□換發船舶無線電臺執照

□增設船舶無線電信設備

請貴處派員於下列約定時間地點審驗船舶無線電信設備：

一、約定時間：     年      月     日    午     時      分

二、約定地點：              岸第               號碼頭

浮筒

此致

□北

國家通訊傳播委員會□中區監理處

□南

船舶所有人：

住址：

電話：（   ）

傳真：（   ）

受委託人（代理經辦廠商）：

住址：

電話：（   ）

傳真：（   ）

上下

向經本會委託或認可之機構申請審驗者：

取得審驗合格報告後，填具申請書直接向本會三區監理處申請船舶無線電臺執照。

繳執照費

六個月內架設完成，提出審驗申

請並繳交審驗費；必要時，另補

齊相關文件。

改善後於期限內通知監理處複驗

收   件

不合格

合格

合格

不合格

連同申請書、審驗報告等

相關資料結案歸檔

核發執照

通知繳執照費並收回架許證

電臺審驗（詳見4.2,4.3）

通知申請者繳架許證費

核發架許證

審   核

檢附相關文件提出架設許可申請

（詳見船舶無線電臺管理辦法第十九條）

收件：