Technical Specifications for New Radio Broadband Terminal Equipment of Mobile Broadband Business

(Unofficial Translation*)

National Communications Commission

April 21 2020

Technical Specifications for New Radio Broadband Terminal Equipment of Mobile Broadband Business

1.	Legal Basis

The Specifications are established on Paragraph 1, Article 42 of the Telecommunications Act.

2.	Scope of Application

The Specifications apply to the type approval for the handheld, vehicular or mobile broadband terminals for new radio (NR) of mobile broadband services and fixed wireless access terminals of mobile broadband services. Depending on terminal duplexing, the frequency division duplex (FDD) and time division duplex (TDD) are available depending on and operate on the following frequency bands:

2.1	Frequency Division Duplex:

2.1.1	Frequency range 1 (FR1):

700 megahertz (MHz hereafter) band (703 MHz～748 MHz for uplink and 758 MHz～803 MHz for downlink), 900 MHz band (885 MHz～915 MHz for uplink and 930 MHz～960 MHz for downlink), 1800 MHz band (1710 MHz～1785 MHz for uplink and 1805 MHz～1880 MHz for downlink), 2100 MHz band (1920 MHz～1980 MHz for uplink and 2110 MHz～2170 MHz for downlink), 2500 MHz and 2600 MHz bands (2500 MHz～2570 MHz for uplink and 2620 MHz～2690MHz for downlink).

2.2	Time Division Duplex:

2.2.1	Frequency range 1 (FR1):

2500 MHz and 2600 MHz bands (2500 MHz～2570 MHz, 2570 MHz～2620 MHz, 2620MHz～2690 MHz), 3500 MHz band (3300 MHz～3570 MHz).

2.2.2	Frequency range 2 (FR2):

28000 MHz band (27000 MHz～29500MHz).

3.	Technical Standards

The Specifications are established by referencing the National Standards, including CNS14958-1, CNS14959, CNS14336-1, CNS13438, CNS15285, CNS15364, and other applicable international technical standards.

4.	Definitions

4.1	Handheld terminal:

A terminal that is used on the move in the normal operating mode with the transmission source less than 20 cm from human body.

4.2	Vehicular or mobile terminal:

A terminal that is used on the move at a non-specific location in the normal operating mode with the transmission source more than 20 cm from human body.

4.3	Fixed wireless access terminal (not handheld high-power):

A terminal that is used at a specific fixed location in the normal operating mode.

5.	Conditions for Test Environment

5.1	Temperature and Relative Humidity:

The conditions for test environment in 6.1 through 6.5 shall meet the following:

|  | FR1 | FR2 |
| --- | --- | --- |
| Normal environment | Temperature : +15℃ to +35℃ Relative Humidity : 25% to 75% | Temperature: +15℃ to +35℃ Relative Humidity: 25% to 75% |
| Extreme environment | Temperature: -10℃ to +55℃ IEC 60068-2-1 and IEC 60068-2-2 shall be met for additional requirements. | Temperature: -10℃ to +55℃ IEC 60068-2-1 and IEC 60068-2-2 shall be met for additional requirements. |

Outside this temperature range, the terminal, if powered on, shall not make ineffective use of the radio frequency band in Article 2.

5.2	Voltage:

The voltage of power to a terminal shall be between lower and higher extreme voltages. The applicant for terminal type approval shall declare the nominal voltage, lower extreme voltage, higher extreme voltage and shutdown voltage. In case that a terminal is capable of operating one or more power sources, the lower extreme voltage shall not be higher than the limits shown in the table below and the higher extreme voltage shall not be lower than the limits shown in the table below.

| Power source | Lower extreme voltage | Higher extreme voltage | Normal conditions voltage |
| --- | --- | --- | --- |
| AC mains | 0.9 × nominal | 1.1 × nominal | nominal |
| Regulated lead acid battery | 0.9 × nominal | 1.3 × nominal | 1.1 × nominal |
| Non regulated batteries: Leclanché Lithium Mercury/nickel & cadmium | 0.85 × nominal 0.95 × nominal 0.90 × nominal | nominal 1.1 × nominal 1.1 × nominal | nominal 1.1 × nominal nominal |

For the voltage of power source lower than the lower extreme voltage shown in the table above or higher than the higher extreme voltage shown in the table above, the terminal, if powered on, shall not make ineffective use of the radio frequency band in Article 2.

In particular, the terminal shall inhibit all RF transmissions when the power supply voltage is below the manufacturer declared shutdown voltage.

6.	Tests to Be Performed and Criteria

6.1	Transmitter power:

6.1.1	FR1:

6.1.1.1	Terminal maximum output power:

6.1.1.1.1	Terminal power class 2: 26 dBm;

6.1.1.1.2	Terminal power class 3: 23 dBm;

6.1.1.1.3	The frequency bands applicable for power classes and allowable tolerance shall meet Table 1, where the test tolerances (TTs) are shown in Table 2.

6.1.1.2	Test method:

Three frequencies (low, mid and high) are tested in accordance with Table 3. The lowest, mid and highest operating bandwidths are tested.

6.1.2	FR2:

6.1.2.1	Effective isotropic radiated power (EIRP) limits:

6.1.2.1.1	The limit is 43 dBm for handheld terminals;

6.1.2.1.2	The limit is 43 dBm for vehicular or mobile terminals;

6.1.2.1.3	The limit is 55 dBm for fixed wireless access terminals.

6.1.2.2	Test method:

Three frequencies (low, mid and high) are tested in accordance with Table 4. The lowest, 100MHz, and highest operating bandwidths are tested.

6.2	Frequency Error

6.2.1	FR1:

6.2.1.1	Limits:

The carrier frequency shall be within ±0.1 part per million (PPM) of the major frequency of channel.

6.2.1.2	Test method:

The test is performed on the highest operating bandwidth in the mid range Frequency according to Table 5.

6.2.2	FR2:

6.2.2.1	Limits:

The carrier frequency shall be within ±0.1 PPM of the major frequency of channel.

6.2.2.2	Test method:

The test channel is the mid range channel. The test is performed on the highest operating bandwidth according to Table 6.

6.3	Adjacent channel leakage ratio (ACLR)

6.3.1	FR1:

6.3.1.1	NR adjacent channel leakage power ratio (NRACLR) is the ratio of the filtered mean power centered on the assigned NR channel frequency to the filtered mean power centered on an adjacent NR channel frequency at nominal channel spacing.

6.3.1.1.1	Limits: if the measured adjacent channel power is greater than –50 dBm then the measured NR ACLR shall be higher than the limits in Table 7, where the test tolerances (TT) are shown in Table 8.

6.3.1.1.2	Test method:

The measurement bandwidth is specified in Table 9. A rectangular filter is used. The test is performed on the lowest and highest operating bandwidths on low and high channels according to Table 10.

6.3.1.2	UTRA adjacent channel leakage power ratio (UTRAACLR) is the ratio of the filtered mean power centered on the assigned NR channel frequency to the filtered mean power centered on an adjacent(s) UTRA channel frequency.

6.3.1.2.1	Limits: if the measured adjacent channel power is greater than –50 dBm, then the measured UTRA ACLR shall be higher than the limits in Table 11.

6.3.1.2.2	Test method:

The UTRA channel power is measured with an RRC filter with roll-off factor α=0.22 and bandwidth of 3.84 MHz. The assigned NR channel power is measured with a rectangular filter with measurement bandwidth specified in Table 9. The test is performed on the lowest and highest operating bandwidths on low and high channels according to Table 10.

6.3.2	FR2:

6.3.2.1	Limits:

If the measured adjacent channel power is greater than –35 dBm then the NRACLR shall be higher than the value specified in Table 12, where the test tolerances (TT) are shown in Table 13.

6.3.2.2	Test method:

The assigned NR channel power and adjacent NR channel power are measured with rectangular filters with measurement bandwidths specified in Table 12. The test is performed on the lowest and highest operating bandwidths on low and high channels according to Table 14.

6.4	Spectrum emission mask

6.4.1	FR1:

6.4.1.1	Limits:

The specified values for spectrum mask in Table 15 shall be met, where the test tolerances (TT) are shown in Table 16.

6.4.1.2	Test method:

6.4.1.2.1	The spectrum emission limits vary depending on the Δ frequency of out-of-band emission (ΔfOOB). For measurement, the resolution bandwidth shall not be smaller than the settings in Table 15.

6.4.1.2.2	The test is performed on the lowest and highest operating bandwidths on low and high channels according to Table 17.

6.4.2	FR2:

6.4.2.1	Limits:

The general specified values for NR spectrum emission mask in Table 18 for FR2 shall be met, where the test tolerances (TT) are shown in Table 19.

6.4.2.2	Test method:

6.4.2.2.1	The resolution bandwidth for measurement shall not be smaller the settings in Table 18. The measurement is performed for total radiated power.

6.4.2.2.2	The test is performed on the lowest and highest operating bandwidths on the medium channel according to Table 20.

6.5	Spurious emissions

6.5.1	FR1:

6.5.1.1	Limits:

The limits for spurious emission shall meet those shown in Table 21.

6.5.1.2	Test method:

6.5.1.2.1	Unless otherwise stated, the spurious emission limits apply for the frequency ranges that are more than FOOB (MHz) in Table 22 from the edge of the channel bandwidth. For measurement, the resolution bandwidth shall not be smaller than the settings in Table 21. FOOB is the boundary between the NR out of band emission and spurious emission domains.

6.5.1.2.2	The test is performed on the lowest, medium and highest operating bandwidths on low, medium and high channels according to Table 23.

6.5.2	FR2:

6.5.2.1	Limits:

6.5.2.1.1	General limits:

The limits for spurious emission shall meet those shown in Table 24.

6.5.2.1.2	Spurious emissions Terminal co-existence limits:

The limits for spurious emission in the co-existence in terminals shall meet the limits shown in Table 25.

6.5.2.1.3	Additional limits: the requirements for additional spurious emission shall be met for the applications of area broadcasting, for example. The limits for additional spurious emission shall meet those shown in Table 26.

6.5.2.2	Test method:

6.5.2.2.1	General limits:

6.5.2.2.1.1		The ΔfOOB in Table 18 is not included in the measurement frequency range. For measurement, the resolution bandwidth shall not be smaller than the settings in Table 24. The measurement is performed for total radiated power.

6.5.2.2.1.2	The test is performed on the highest operating bandwidth on low and high channels according to Table 27.

6.5.2.2.2	Limits for co-existing bandwidths in terminals:

6.5.2.2.2.1	The spurious emission in the co-existing bandwidths in terminals shall meet the limits shown in Table 25. However, the ΔfOOB in Table 18 is not included. The measurement is performed for total radiated power.

6.5.2.2.2.2	The test is performed on the highest operating bandwidth on low and high channels according to Table 27.

6.5.2.2.3	Additional limits:

6.5.2.2.3.1	The limits for additional spurious emission shall meet the limits shown in Table 26. The measurement is performed for total radiated power.

6.5.2.2.3.2	The test is performed on the highest operating bandwidth on low and high channels according to Table 27.

6.6	Limits for Electromagnetic Exposure

6.6.1	This test applies to handheld terminals.

6.6.1.1	FR1:

The standard values of specific absorption rate (SAR) for electromagnetic energy shall meet CNS14959. The limit for SAR for the use of a terminal close to head is 2 W/kg. The measurement procedure specified in IEC 62209-1 shall be used.

6.6.1.2	FR2:

The limits for power density (PD) shall meet the requirement of 1.0 mW/cm². The measurement procedure specified in IEC TR 63170 shall be used.

6.6.2	This test applies to vehicular , mobile or fixed wireless access terminals.

6.6.2.1	Limits for Maximum Permissible Exposure (MPE):

0.35 mW/cm² for 700 MHz band;

0.45 mW/cm² for 900 MHz band;

0.9 mW/cm² for 1800 MHz band;

1.0 mW/cm² for 2100 MHz, 2500 MHz, 2600 MHz, 3500MHz and 28GHz bands.

The measurement is performed at a distance of 20 cm or the distance claimed by the terminal manufacturer for human activities in the vicinity of the terminal antenna.

6.7	Electromagnetic Compatibility (EMC)

CNS13438 or any other applicable standards established by the competent authority shall be met.

6.8	Electrical Safety

CNS14336-1 or any other applicable standards established by the competent authority shall be met.

6.9	Handheld Terminal Connection Interface, Power Adaptor Connection Interface, Charging Cord and Power Adaptor

6.9.1	This test applies to mobile phones.

6.9.2	The basic structure shown in Figure B.1 of CNS15285 shall be used for the connection interface. An adapting charging cord or adaptor shall be used for mobile phones with a socket for a specific mobile terminal in Figure B.1.

6.9.3	The rated charging current range for the power adaptor shall meet CNS15285 B.2.1(c).

6.9.4	Handheld terminal connection interface, power adaptor connection interface, charging cord and power adaptor shall meet the general characteristics in CNS15285 B.2.2. The no-load power consumption of power adaptor shall be smaller than 0.15W.

6.9.5	Rechargeable batteries shall be used in mobile phones. CNS 15364 shall be met.

6.9.6	The insulation materials used on handheld terminal connection interface and power adaptor connection interface shall meet IEC 60695-11-10 or be of Class V-2 or higher in UL 94.

6.9.7	The fire rating of the charging cord materials shall meet IEC 60332-1 or be of Class VW-1 or higher in UL 1581.

6.10	Message Reception from Public Warning System

6.10.1	This test applies to handheld terminals that are equipped with access to voice service provided a mobile broadband service provider.

6.10.2	The public warning system (PWS) refers to a system that transmits CBS message identifier and contents from a base station to a certain area using the cell broadcast service (CBS) of mobile communication system.

6.10.3	A terminal shall be provided with functions to receive message identifiers and display message contents, such as:

6.10.3.1	The language of the contents PWS alerts, message identifier, classification, preset receiving on or off, and the options of users, etc shall comply with the provisions of Table 28.

6.10.3.2	When a terminal set to receive messages receives a PWS message, the content of the message shall be displayed explicitly with the classification of message identifier shown at the title of the message content; see Figure 1 for an example.

6.10.3.3	 The message identifier shall be tested together with the following message contents: 6.10.3.3.1 and 6.10.3.3.3 shall be tested; 6.10.3.3.2 shall be tested starting from January 1 2021; however, the test may be scheduled on an earlier day if such a request is made by the applicant for the type approval of terminal.

6.10.3.3.1	For a terminal with an interface in Chinese, the message content shall be: [本訊息為災防告警訊息測試]業者配合政府政策，已建置細胞廣播系統，目前在發送測試用災防告警細胞廣播訊息，造成不便，敬請見諒，國家通訊傳播委員會關心您。

6.10.3.3.2	For a terminal with an interface in Chinese and English, the message content shall be shown in both Chinese and English, as follows: [災防告警測試]業者依照政府政策，測試災防告警，造成不便，敬請見諒，國家通訊傳播委員會關心您。[Public warning testing] Your mobile phone operator complies with government policies and tests public warning. We apologize for any inconvenience and appreciate your kind understanding. National Communications Commission

6.10.3.3.3	For a terminal with an interface in English, the message content shall be: [The message is for public warning message testing] Your mobile phone operator has set up cell broadcasting systems for transmitting public warning messages. Now this service is still in trial. We apologize for any inconvenience it may cause and appreciate your kind understanding.

National Communications Commission

6.10.3.4	The terminal shall allow user to view the content of previous message received.

6.10.3.5	Users are not allowed to forward a PWS message received by the terminal or edit the content of the message.

6.10.4	Audio signals:

6.10.4.1	The audio signal shall be categorized into two kinds of signal: audio attention signal and audio general signal:

6.10.4.1.1	Audio attention signal:

6.10.4.1.1.1	The audio attention signal shall consist of a special audio frequency and interval, and the audio attention signal shall not be set up by the user or modified:

6.10.4.1.1.1.1	Special audio frequency: for the function of audio mixing, the signal shall be generated by mixing the fundamental frequencies of 853 hertz (Hz) and 960 Hz; for the function of monotone, the signal shall be generated using a single tone of 960 Hz.

6.10.4.1.1.1.2	Special interval: the audio attention signal consists of two sections with an interval of 0.5 seconds in between; the composition of the signal is a sound lasting 2 seconds + a second sound lasting 1 second with an interval of 0.5 second between the sounds.

6.10.4.1.1.1.3	The pattern of the audio attention signal is provided in Figure 2.

6.10.4.1.1.2	The audio alert signal is used only for PWS broadcasting.

6.10.4.1.2	General audio signal: the general audio signal contains no special audio frequency and interval and can be defined or altered by users; i.e. the audio signals generated by the terminal when a typical message is received.

6.10.4.2	When to generate: for a terminal set to receive message identifiers, when a PWS message is received, an audio signal shall be generated corresponding to the message identifier and user’s definitions, as shown in Table 29.

6.10.4.3	The default shall be that the audio signals are activated, and the user is allowed to deactivate or activate.

6.10.4.4	When the terminal generates an audio signal, the user may terminate the signal before it ends.

6.10.5	Vibration cadence:

6.10.5.1	For vibration cadence, there are vibration attention cadence and general vibration cadence:

6.10.5.1.1	Vibration attention cadence:

6.10.5.1.1.1	An vibration attention cadence shall be provided with a special interval. The vibration attention cadence shall not be set up by the user or modified:

6.10.5.1.1.1.1	Special interval: the vibration attention cadence consists of two sections of vibrations with an interval of 0.5 second in between. Every section of vibration is made up of one vibration of 2 seconds, followed by two vibrations of 1 second with an interval of 0.5 second between vibrations.

6.10.5.1.1.1.2	The temporal pattern of vibration attention cadence in Figure 3.

6.10.5.1.1.2	The vibration attention cadence is used only for PWS broadcasting.

6.10.5.1.1.3	The vibration attention cadence and audio attention signal does not need to be synchronized.

6.10.5.1.2	General vibration signal: The general vibration cadence shall not have special interval of vibration when a general message is received by the terminal.

6.10.5.2	When to generate: for a terminal set to receive message identifiers, when a PWS message is received, a vibration shall be generated corresponding to the message identifier and user’s definitions, as shown in Table 29.

6.10.5.3	The vibration cadence is considered to be an opt-out by the user with the initial default configuration being that all emergency alerts are enabled.

6.10.5.4	When the terminal generates a vibration signal, the user may terminate the signal before it ends.

6.10.6	The presentation of the received PWS alert message should take priority over other mobile device functions. The PWS alert message shall not preempt an active voice or data session.

6.10.7	The processing of receiving the duplicate PWS message:

6.10.7.1	Duplicate PWS alert message refers to PWS alert messages with the same message identifier and serial number, indicating that they have been sent repeated. The definition of serial number shall refer to the technical standard 3GPP TS 23.041.

6.10.7.2	Where the equipment receives duplicate PWS alert message from the base station, it shall not show the message content or generate signal and vibration.

6.10.8	For a terminal with a hardware interface of mobile broadband service terminal or Generation 3 mobile telecommunications terminal, the PWS message receiving function of the terminal shall meet the requirements specified in 6.10 of the Specifications.

6.11	IMEI Number and Guarantee of uniqueness

The IMEI number is read and recorded by test instrument. The applicant shall submit the guarantee of IMEI uniqueness.

7.	Test Requirements

7.1	For the test procedures and limits specified in the Specifications, the requirements in the latest version of 3GPP TS 38.101-1, 3GPP TS 38.101-2, 3GPP TS 38.521-1 and 3GPP TS 38.521-2, if any, may be adopted.

7.2	Unless otherwise specified in the Specifications, Article 5 of the Technical Specifications for Low-Power Radio Frequency Machines shall apply to the test methods for the tests specified in 6.1, 6.2 and 6.5. For test procedures, the reference procedure for transmitter test in Appendix 1 of the Technical Specifications for Low-Power Radio Frequency Machines shall apply.

7.3	6.7 through 6.9 of the Specifications shall be performed jointly with power adaptor and charging cord; however, for the submitted power adaptor and charging cord for which the type approval has been obtained, the tests for power adaptor and charging cord specified in 6.9 of the Specifications may be waived with the presence of approval certificate and test report.

8.	Warning indication

8.1	Electromagnetic warning indication

8.1.1	The content of warning shall be similar to: “Use with caution to minimize electromagnetic impacts.”

8.1.2	Indication: the warning shall be labeled visibly on the body of terminal and indicated on the outer package of terminal and in the user’s instructions.

8.2	Warning Indication for Electromagnetic Exposure

8.2.1	For Handheld Mobile Terminals

8.2.1.1	The content of warning for 6GHz or lower shall be similar to: “Standard SAR value: ____ W/kg, actual value measured on product: ____ W/kg.”

8.2.1.2	The content of warning for 6GHz or higher shall be similar to: “Standard PD: 1.0 mW/cm2, actual value measured on product: ____ mW/cm2.”

8.2.2	For Vehicular, Mobile or Fixed Wireless Access Terminals

The content of warning shall be similar to: “Standard MPE: ____ mW/cm2, actual value measured on product: ____ mW/cm2; it is advised to keep the antenna at least ____ cm away from human body when using the device.”

8.2.3	Indication: the warning shall be labeled visibly on the body of terminal and indicated on the outer package of terminal and in the user’s instructions.

Table 1 FR1 Maximum Output Power test requirement (see 3GPP TS 38.521-1 Table 6.2.1.5-1 and Table 6.2.1.5-2)

| NR uplink frequency band (MHz) | Class 2 (dBm) | Tolerance (dB) | Class 3 (dBm) | Tolerance (dB) |
| --- | --- | --- | --- | --- |
| 1920～1980 |  |  | 23 | +2+TT/-2-TT |
| 1710～1785 |  |  | 23 | +2+TT/-2-TT (note) |
| 2500～2570 |  |  | 23 | +2+TT/-2-TT (note) |
| 885～915 |  |  | 23 | +2+TT/-2-TT (note) |
| 703～748 |  |  | 23 | +2/-2.5 |
| 2500～2690 | 26 | +2+TT/-3-TT (note) | 23 | +2+TT/-2-TT (note) |
| 3300～3570 | 26 | +2+TT/-3-TT | 23 | +2+TT/-3-TT |
| Note: Refers to the transmission bandwidths confined within FUL_low and FUL_low + 4 MHz or FUL_high – 4 MHz and FUL_high, the maximum output power requirement is relaxed by reducing the lower tolerance limit by 1.5 dB |

Table 2 Test tolerance (TT) for FR1 Terminal maximum output power (see 3GPP 38.521-1 Table 6.2.1.5-3)

|  | f ≤ 3.0GHz | 3.0GHz < f ≤ 4.2GHz | 4.2GHz < f ≤ 6.0GHz |
| --- | --- | --- | --- |
| Channel bandwidth ≤ 40MHz | 0.7 dB | 1.0 dB | 1.0 dB |
| 40MHz < channel bandwidth ≤ 100MHz | 1.0 dB | 1.0 dB | 1.0 dB |

Table 3 Test Configuration Table for FR1 transmitter output power (see 3GPP 38.521-1 Table 6.2.1.4.1-1)

| Initial conditions |
| --- |
| Test environment | Normal |
| Test channel | Low range, Mid range, High range |
| Test channel bandwidth | Lowest, Mid, Highest |
| Subcarrier spacing | Lowest, Highest |
| Test parameters |
| Test ID | Downlink Configuration | Uplink Configuration |
|  | Not applicable | Modulation (note 2) | RB allocation (note 1) |
| 1 |  | DFT-s-OFDM PI/2 BPSK | Inner Full |
| 2 |  | DFT-s-OFDM PI/2 BPSK | Inner 1RB Left |
| 3 |  | DFT-s-OFDM PI/2 BPSK | Inner 1RB Right |
| 4 |  | DFT-s-OFDM QPSK | Inner Full |
| 5 |  | DFT-s-OFDM QPSK | Inner 1RB Left |
| 6 |  | DFT-s-OFDM QPSK | Inner 1RB Right |
| Note 1: The specific configuration of each resource block (RB) distribution is defined in 3GPP TS 38.521-1 Table 6.1-1. Note 2: the DFT-s-OFDM PI/2 BPSK test applies only for UEs which supports half Pi BPSK in FR1. |

Table 4 Test Configuration Table for FR2 effective isotropic radiated power (see 3GPP 38.521-2 Table 6.2.1.1.4.1-1)

| Default conditions |
| --- |
| Test environment | Normal |
| Test Frequencies | Low range, Mid Range, High range |
| Test channel bandwidth | Lowest, 100MHz, highest |
| Subcarrier spacing | 120 kHz |
|  | Test parameters |
| Test ID | Channel bandwidth | Subcarrier spacing | Downlink Configuration | Uplink Configuration |
|  |  | Default | Not applicable | Modulation | RB allocation (note) |
| 1 | 50 MHz |  |  | DFT-s-OFDM QPSK | Inner_Full |
| 2 | 100 MHz |  |  |  |  |
| 3 | 200 MHz |  |  |  |  |
| 4 | 400 MHz |  |  |  |  |
| Note: The specific configuration of each RF allocation is defined in 3GPP TS 38.521-2 Table 6.1-1. |

Table 5 Test Configuration Table for FR1 frequency error (see 3GPP TS 38.521-1 Table 6.4.1.4.1-1)

| Initial conditions |
| --- |
| Test environment | Normal environment + normal voltage, lower extreme temperature + lower extreme voltage, lower extreme temperature + higher extreme voltage, higher extreme temperature + lower extreme voltage, higher extreme temperature + higher extreme voltage |
| Test Frequencies | Mid range |
| Test channel bandwidth | Highest |
| Subcarrier spacing | Lowest |
| Test parameters |
|  | Downlink Configuration | Uplink Configuration |
| Test ID | Modulation | RB allocation | Modulation | RB allocation |
| 1 | CP-OFDM QPSK | Full RB (note 1) | DFT-s-OFDM QPSK | REFSENS (note 2) |
| Note 1: Full RB allocation shall be used per each SCS and channel BW as specified in 3GPP 38.521-1 Table 7.3.2.4.1-2. Note 2: The reference sensitivity (REFSENS) refers to 3GPP 38.521-1 Table 7.3.2.4.1-3 which defines uplink RB configuration and start RB location for each SCS, channel BW and NR band. |

Table 6 Test Configuration Table for FR2 frequency error (see 3GPP TS 38.521-2 Table 6.4.1.4.1-1)

| Initial conditions |
| --- |
| Test environment | Normal environment + normal voltage, lower extreme temperature + normal voltage, higher extreme temperature + normal voltage |
| Test Frequencies | Mid range |
| Test channel bandwidth | Highest |
| Test SCS as specified in 3GPP 38.521-1 Table 5.3.5-1 | Lowest |
| Test parameters |
| Test ID | Downlink Configuration | Uplink Configuration |
|  | Modulation | RB allocation | Modulation | RB allocation |
| 1 | CP-OFDM QPSK | Full RB (note 1) | DFT-s-OFDM QPSK | REFSENS (note 2) |
| Note 1: Full RB allocation shall be used per each SCS and channel BW as specified in 3GPP 38.521-1 Table 7.3.2.4.1-2. Note 2: The reference sensitivity (REFSENS) refers to 3GPP 38.521-1 Table 7.3.2.4.1-3 which defines uplink RB configuration and start RB location for each SCS, channel BW and NR band. |

Table 7 NR ACLR requirement for FR1 (see 3GPP TS 38.521-1 Table 6.5.2.4.1.5-2)

|  | Terminal power class 2 | Terminal power class 3 |
| --- | --- | --- |
| NR ACLR | 31 - TT dB | 30 - TT dB |

Table 8 Test tolerance (TT) of FR1 NR ACLR (see 3GPP TS 38.521-1 Table 6.5.2.4.1.5-3)

|  | f ≤ 3.0GHz | 3.0GHz < f ≤ 4.2GHz | 4.2GHz < f ≤ 6.0GHz |
| --- | --- | --- | --- |
| BW ≤ 100MHz | 0.8 dB | 0.8 dB | 0.8 dB |

Table 9 FR1 NRACLR measurement bandwidth (see 3GPP 38.521-1 Table 6.5.2.4.1.5-1)

| NR Channel bandwidth / NR ACLR measurement bandwidth |
| --- |
|  | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz |
| NR ACLR measurement bandwidth (MHz) | 4.515 | 9.375 | 14.235 | 19.095 | 23.955 | 28.815 | 38.895 | 48.615 | 58.35 | 78.15 | 88.23 | 98.31 |

Table 10 FR1 ACLR Test Configuration Table (see 3GPP TS 38.521-1 Table 6.5.2.4.1.4.1-1)

| Initial conditions |
| --- |
| Test environment | Normal environment + normal voltage |
| Test channel | Low range, High range |
| Test channel bandwidth | Lowest, Highest |
| Subcarrier spacing | Lowest and highest |
| Channel bandwidth test parameters |
| Test ID | Frequency | Channel bandwidth | Subcarrier spacing | Downlink Configuration | Uplink Configuration |
|  |  | Default | Default | N/A for Adjacent Channel Leakage Ratio test case | Modulation (note 2) | RB allocation (note 1) |
| 1 (note 3) | Default |  |  |  | DFT-s-OFDM PI/2 BPSK | Inner_Full |
| 2 (note 3) | Low channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Edge_1RB_Left |
| 3 (note 3) | High channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Edge_1RB_Right |
| 4 (note 3) | Default |  |  |  | DFT-s-OFDM PI/2 BPSK | Outer_Full |
| 5 (note 4) | Default |  |  |  | DFT-s-OFDM PI/2 BPSK | Inner_Full |
| 6 (note 4) | Low channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Edge_1RB_Left |
| 7 (note 4) | High channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Edge_1RB_Right |
| 8 (note 4) | Default |  |  |  | DFT-s-OFDM PI/2 BPSK | Outer_Full |
| 9 | Default |  |  |  | DFT-s-OFDM QPSK | Inner_Full |
| 10 | Low channel |  |  |  | DFT-s-OFDM QPSK | Edge_1RB_Left |
| 11 | High channel |  |  |  | DFT-s-OFDM QPSK | Edge_1RB_Right |
| 12 | Default |  |  |  | DFT-s-OFDM QPSK | Outer_Full |
| 13 | Default |  |  |  | DFT-s-OFDM 16 QAM | Inner_Full |
| 14 | Low channel |  |  |  | DFT-s-OFDM 16 QAM | Edge_1RB_Left |
| 15 | High channel |  |  |  | DFT-s-OFDM 16 QAM | Edge_1RB_Right |
| 16 | Default |  |  |  | DFT-s-OFDM 16 QAM | Outer_Full |
| 17 | Low channel |  |  |  | DFT-s-OFDM 64 QAM | Edge_1RB_Left |
| 18 | High channel |  |  |  | DFT-s-OFDM 64 QAM | Edge_1RB_Right |
| 19 | Default |  |  |  | DFT-s-OFDM 64 QAM | Outer_Full |
| 20 | Low channel |  |  |  | DFT-s-OFDM 256 QAM | Edge_1RB_Left |
| 21 | High channel |  |  |  | DFT-s-OFDM 256 QAM | Edge_1RB_Right |
| 22 | Default |  |  |  | DFT-s-OFDM 256 QAM | Outer_Full |
| 23 | Default |  |  |  | CP-OFDM QPSK | Inner_Full |
| 24 | Low channel |  |  |  | CP-OFDM QPSK | Edge_1RB_Left |
| 25 | High channel |  |  |  | CP-OFDM QPSK | Edge_1RB_Right |
| 26 | Default |  |  |  | CP-OFDM QPSK | Outer_Full |
| 27 | Default |  |  |  | CP-OFDM 16 QAM | Inner_Full |
| 28 | Low channel |  |  |  | CP-OFDM 16 QAM | Edge_1RB_Left |
| 29 | High channel |  |  |  | CP-OFDM 16 QAM | Edge_1RB_Right |
| 30 | Default |  |  |  | CP-OFDM 16 QAM | Outer_Full |
| 31 | Low channel |  |  |  | CP-OFDM 64 QAM | Edge_1RB_Left |
| 32 | High channel |  |  |  | CP-OFDM 64 QAM | Edge_1RB_Right |
| 33 | Default |  |  |  | CP-OFDM 64 QAM | Outer_Full |
| 34 | Low channel |  |  |  | CP-OFDM 256 QAM | Edge_1RB_Left |
| 35 | High channel |  |  |  | CP-OFDM 256 QAM | Edge_1RB_Right |
| 36 | Default |  |  |  | CP-OFDM 256 QAM | Outer_Full |
| Note 1: The specific configuration of each RF allocation is defined in 3GPP TS 38.521-1 Table 6.1-1. Note 2: DFT-s-OFDM PI/2 BPSK test applies only for UEs which supports half Pi BPSK in FR1. Note 3: For Power Class 3 testing, UE operating in TDD mode with PI/2 BPSK modulation, and UE indicating support for UE capability powerBoosting-pi2BPSK, the IE powerBoostPi2BPSK is set to 1 for frequency band at 2500-2690 MHz (n41)/3300-3570 MHz (n78). Note 4: For Power Class 3 testing, UE operating in FDD mode, or in TDD mode in bands other than 2500-2690 MHz (n41)/3300-3570 MHz (n78) , or in TDD mode the IE powerBoostPi2BPSK is set to 0 for bands 3300-3570 MHz (n78). |

Table 11 UTRA ACLR requirement for FR1 (UTRAACLR) (see 3GPP 38.521-1 Table 6.5.2.4.2.5-2)

|  | Terminal power class 3 (note 1) |
| --- | --- |
| UTRAACLR1 (note 2) | 33 dB - TT |
| UTRAACLR2 (note 3) | 36 dB - TT |
| Note 1: TT = 0.8 dB。 Note 2: UTRAACLR1 is first adjacent UTRA channel (UTRAACLR1) which centre frequency is ± 2.5 MHz from NR channel edge. Note 3: UTRAACLR2 is the 2nd adjacent UTRA channel (UTRAACLR2) which centre frequency is ± 7.5 MHz from NR channel edge. |

Table 12 General requirements for NR adjacent channel leakage ratio(NRACLR) for FR2 (see 3GPP TS 38.521-2 Table 6.5.2.3.5-1)

|  | Channel bandwidth |
| --- | --- |
|  | 50 MHz | 100 MHz | 200 MHz | 400 MHz |
| NR ACLR limits | 17+TT dB | 17+TT dB | 17+TT dB | 17+TT dB |
| NR channel measurement bandwidth | 47.52 MHz | 95.04 MHz | 190.08 MHz | 380.16 MHz |
| Adjacent channel centre frequency offset | ±50 MHz | ±100 MHz | ±200 MHz | ±400 MHz |

Table 13 Test tolerance (TT) for NR adjacent channel leakage ratio for FR2 (see 3GPP TS 38.521-2 Table 6.5.2.3.5-1a)

| Test environment (Test Metric) | 23.45GHz ≤ f ≤ 30.3GHz |
| --- | --- |
| Indirect far field (IFF) (quiet zone size ≤ 30 cm) | 4.6 dB |

Table 14 Channel bandwidth test parameters for FR2 NRACLR (see 3GPP TS 38.521-2 Table 6.5.2.3.4.1-1)

| Default Conditions |
| --- |
| Test environment | Normal environment + normal voltage |
| Test Frequencies | Low range, High range |
| Test channel bandwidths | Lowest, Mid, Highest |
| Subcarrier spacing | Lowest and highest |
| Test parameters |
| Test ID | Frequency | Channel bandwidth | SCS | Downlink Configuration | Uplink Configuration |
|  |  | Default | Default | Not applicable | Modulation | RB allocation (note) |
| 1 | Low channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Outer_1RB_Left |
| 2 | High channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Outer_1RB_Right |
| 3 | Default |  |  |  | DFT-s-OFDM PI/2 BPSK | Outer_Full |
| 4 | Low channel |  |  |  | DFT-s-OFDM QPSK | Outer_1RB_Left |
| 5 | High channel |  |  |  | DFT-s-OFDM QPSK | Outer_1RB_Right |
| 6 | Default |  |  |  | DFT-s-OFDM QPSK | Outer_Full |
| 7 | Low channel |  |  |  | DFT-s-OFDM 16 QAM | Outer_1RB_Left |
| 8 | High channel |  |  |  | DFT-s-OFDM 16 QAM | Outer_1RB_Right |
| 9 | Default |  |  |  | DFT-s-OFDM 16 QAM | Outer_Full |
| 10 | Default |  |  |  | DFT-s-OFDM 64 QAM | Outer_Full |
| 11 | Low channel |  |  |  | CP-OFDM QPSK | Outer_1RB_Left |
| 12 | High channel |  |  |  | CP-OFDM QPSK | Outer_1RB_Right |
| 13 | Default |  |  |  | CP-OFDM QPSK | Outer_Full |
| Note: The specific configuration of each RF allocation is defined in 3GPP TS 38.521-2 Table 6.1-1. |

Table 15 FR1 spectrum emission mask specifications (see 3GPP TS 38.521-1 Table 6.5.2.2.5-1)

| Emission limits (dBm)/Channel bandwidth |
| --- |
| ΔfOOB (MHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Resolution bandwidth |
| ± 0-1 | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT |  |  |  |  |  | 1 % of Channel bandwidth |
| ± 0-1 |  |  |  |  |  |  |  | -24 +TT | -24 +TT | -24 +TT | -24 +TT | -24 +TT | 30 kHz (note 1) |
| ± 1-5 | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | -10 +TT | 1 MHz (note 2) |
| ± 5-6 | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT | -13 +TT |  |
| ± 6-10 | -25 +TT |  |  |  |  |  |  |  |  |  |  |  |  |
| ± 10-15 |  | -25 +TT |  |  |  |  |  |  |  |  |  |  |  |
| ± 15-20 |  |  | -25 +TT |  |  |  |  |  |  |  |  |  |  |
| ± 20-25 |  |  |  | -25 +TT |  |  |  |  |  |  |  |  |  |
| ± 25-30 |  |  |  |  | -25 +TT |  |  |  |  |  |  |  |  |
| ± 30-35 |  |  |  |  |  | -25 +TT |  |  |  |  |  |  |  |
| ± 35-40 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ± 40-45 |  |  |  |  |  |  | -25 +TT |  |  |  |  |  |  |
| ± 45-50 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ± 50-55 |  |  |  |  |  |  |  | -25 +TT |  |  |  |  |  |
| ± 55-60 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ± 60-65 |  |  |  |  |  |  |  |  | -25 +TT |  |  |  |  |
| ± 65-80 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ± 80-85 |  |  |  |  |  |  |  |  |  | -25 +TT |  |  |  |
| ± 85-90 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ± 90-95 |  |  |  |  |  |  |  |  |  |  | -25 +TT |  |  |
| ± 95-100 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| ± 100-105 |  |  |  |  |  |  |  |  |  |  |  | -25 +TT |  |
| Note 1: The first and last measurement position with a 30 kHz filter is at ΔfOOB equals to 0.015 MHz and 0.985 MHz. Note 2: At the boundary of spectrum emission limit, the first and last measurement position with a 1 MHz filter is the inside of +0.5MHz and -0.5MHz, respectively. Note 3: The measurements are to be performed above the upper edge of the channel and below the lower edge of the channel specified in Article 2 of the Specifications for applicable frequency bands. Note 4: Test Tolerance(TT) for each frequency and channel bandwidth is specified in Table 16. |

Table 16 Test tolerance (TT) for FR1 spectrum emission mask (see 3GPP TS 38.521-1 Table 6.5.2.2.5-2)

|  | f ≤ 3.0GHz | 3.0GHz < f ≤ 4.2GHz | 4.2GHz < f ≤ 6.0GHz |
| --- | --- | --- | --- |
| BW ≤ 100MHz | 1.5 dB | 1.8 dB | 1.8 dB |

Table 17 Channel bandwidth test parameters for FR1 spectrum emission mask (see 3GPP TS 38.521-1 Table 6.5.2.2.4.1-1)

| Default Conditions |
| --- |
| Test environment | Normal environment + normal voltage |
| Test Frequencies | Low range, High range |
| Test channel bandwidths | Lowest and highest |
| Subcarrier spacing | Lowest and highest |
| Test ID | Test Parameters for Channel Bandwidths |
|  | Frequency | Channel bandwidth | Subcarrier spacing | Downlink Configuration | Uplink Configuration |
|  |  | Default | Default | Not applicable | Modulation (note 2) | RB allocation (note 1) |
| 1 (note 3) | Low channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Edge_1RB_Left |
| 2 (note 3) | High channel |  |  |  | DFT-s-OFDM PI/2 BPSK | Edge_1RB_Right |
| 3 (note 3) | Default |  |  |  | DFT-s-OFDM PI/2 BPSK | Outer_Full |
| 4 | Low channel |  |  |  | DFT-s-OFDM QPSK | Edger_1RB_Left |
| 5 | High channel |  |  |  | DFT-s-OFDM QPSK | Edge_1RB_Right |
| 6 | Default |  |  |  | DFT-s-OFDM QPSK | Outer_Full |
| 7 | Low channel |  |  |  | DFT-s-OFDM 16 QAM | Edge_1RB_Left |
| 8 | High channel |  |  |  | DFT-s-OFDM 16 QAM | Edge_1RB_Right |
| 9 | Default |  |  |  | DFT-s-OFDM 16 QAM | Outer_Full |
| 10 | Low channel |  |  |  | DFT-s-OFDM 64 QAM | Edge_1RB_Left |
| 11 | High channel |  |  |  | DFT-s-OFDM 64 QAM | Edge_1RB_Right |
| 12 | Default |  |  |  | DFT-s-OFDM 64 QAM | Outer_Full |
| 13 | Low channel |  |  |  | DFT-s-OFDM 256 QAM | Edge_1RB_Left |
| 14 | High channel |  |  |  | DFT-s-OFDM 256 QAM | Edge_1RB_Right |
| 15 | Default |  |  |  | DFT-s-OFDM 256 QAM | Outer_Full |
| 16 | Low channel |  |  |  | CP-OFDM QPSK | Edge_1RB_Left |
| 17 | High channel |  |  |  | CP-OFDM QPSK | Edge_1RB_Right |
| 18 | Default |  |  |  | CP-OFDM QPSK | Outer_Full |
| 19 | Low channel |  |  |  | CP-OFDM 16 QAM | Edge_1RB_Left |
| 20 | High channel |  |  |  | CP-OFDM 16 QAM | Edge_1RB_Right |
| 21 | Default |  |  |  | CP-OFDM 16 QAM | Outer_Full |
| 22 | Low channel |  |  |  | CP-OFDM 64 QAM | Edge_1RB_Left |
| 23 | High channel |  |  |  | CP-OFDM 64 QAM | Edge_1RB_Right |
| 24 | Default |  |  |  | CP-OFDM 64 QAM | Outer_Full |
| 25 | Low channel |  |  |  | CP-OFDM 256 QAM | Edge_1RB_Left |
| 26 | High channel |  |  |  | CP-OFDM 256 QAM | Edge_1RB_Right |
| 27 | Default |  |  |  | CP-OFDM 256 QAM | Outer_Full |
| Note 1: The specific configuration of each RF allocation is defined in 3GPP TS 38.521-1 Table 6.1-1. Note 2: DFT-s-OFDM PI/2 BPSK test applies only for terminals which supports half Pi BPSK in FR1.. Note 3: For Power Class 3 testing, include two steps for terminals operating on 2500-2690 MHz (n41) / 3300-3570 MHz (n78) , with IE powerBoostPi2BPSK set to 1 and 0 separately. |

Table 18 General NR spectrum emission mask specifications for FR2 (see 3GPP TS 38.521-2 Table 6.5.2.1.5-1)

| Spectrum Emission limits (dBm) / Channel bandwidth |
| --- |
| ΔfOOB (MHz) | 50MHz | 100MHz | 200MHz | 400MHz | Measurement bandwidth |
| ± 0-5 | -5+TT | -5+TT | -5+TT | -5+TT | 1 MHz |
| ± 5-10 | -13+TT | -5+TT | -5+TT | -5+TT | 1 MHz |
| ± 10-20 | -13+TT | -13+TT | -5+TT | -5+TT | 1 MHz |
| ± 20-40 | -13+TT | -13+TT | -13+TT | -5+TT | 1 MHz |
| ± 40-100 | -13+TT | -13+TT | -13+TT | -13+TT | 1 MHz |
| ± 100-200 |  | -13+TT | -13+TT | -13+TT | 1 MHz |
| ± 200-400 |  |  | -13+TT | -13+TT | 1 MHz |
| ± 400-800 |  |  |  | -13+TT | 1 MHz |
| Note 1: see Table 19 for test tolerance (TT). Note 2: At the boundary of spectrum emission limit, the first and last measurement position with a 1 MHz filter is the inside of +0.5MHz and -0.5MHz, respectively. Note 3: The measurements are to be performed above the upper edge of the channel and below the lower edge of the channel, specified in Article 2 of the Specifications for applicable frequency bands. |

Table 19 Test tolerance (TT) for general NR spectrum emission mask specifications for FR2 (see 3GPP TS 38.521-2 Table 6.5.2.1.5-1a)

| Test environment (Test Metric) | 23.45GHz ≤ f ≤ 32.125GHz |
| --- | --- |
| Indirect far field (IFF) (quiet zone size ≤ 30 cm) | 3.21 dB |

Table 20 Test Configuration for FR2 spectrum emission mask (see 3GPP TS 38.521-2 Table 6.5.2.1.4.1-1)

| Initial Conditions |
| --- |
| Test environment | Normal environment + normal voltage |
| Test Frequencies | Mid range |
| Test channel bandwidths | Lowest, Mid, Highest |
| Subcarrier spacing | Lowest and highest |
| Test parameters |
| Test ID | Downlink Configuration | Uplink Configuration |
|  | Not applicable | Modulation | RB allocation (note) |
| 1 |  | DFT-s-OFDM PI/2 BPSK | Outer_1RB_Left |
| 2 |  | DFT-s-OFDM PI/2 BPSK | Outer_1RB_Right |
| 3 |  | DFT-s-OFDM PI/2 BPSK | Outer_Full |
| 4 |  | DFT-s-OFDM QPSK | Outer_1RB_Left |
| 5 |  | DFT-s-OFDM QPSK | Outer_1RB_Right |
| 6 |  | DFT-s-OFDM QPSK | Outer_Full |
| 7 |  | DFT-s-OFDM 16 QAM | Outer_1RB_Left |
| 8 |  | DFT-s-OFDM 16 QAM | Outer_1RB_Right |
| 9 |  | DFT-s-OFDM 16 QAM | Outer_Full |
| 10 |  | DFT-s-OFDM 64 QAM | Outer_1RB_Left |
| 11 |  | DFT-s-OFDM 64 QAM | Outer_1RB_Right |
| 12 |  | DFT-s-OFDM 64 QAM | Outer_Full |
| 13 |  | CP-OFDM QPSK | Outer_1RB_Left |
| 14 |  | CP-OFDM QPSK | Outer_1RB_Right |
| 15 |  | CP-OFDM QPSK | Outer_Full |
| Note: The specific configuration of each RF allocation is defined in 3GPP TS 38.521-1 Table 6.1-1. |

Table 21 Limits for spurious emission for FR1 (see 3GPP TS 38.521-1 Table 6.5.3.1.3-2)

| Frequency range | Maximum level | Resolution bandwidth | Note |
| --- | --- | --- | --- |
| 9 kHz ≤ f < 150 kHz | -36 dBm | 1 kHz |  |
| 150 kHz ≤ f < 30 MHz | -36 dBm | 10 kHz |  |
| 30 MHz ≤ f < 1000 MHz | -36 dBm | 100 kHz |  |
| 1 GHz ≤ f < 12.75 GHz | -30 dBm | 1 MHz |  |
|  | -25 dBm | 1 MHz | 3 |
| 12.75GHz≤f< 5 x highest harmonics of the maximum UL operating frequency, in GHz | -30 dBm | 1 MHz | 1 |
| 12.75 GHz < f < 26 GHz | -30 dBm | 1 MHz | 2 |
| Note 1: Applies for Band that the upper frequency edge of the UL Band more than 2.69 GHz Note 2: Applies for Band that the upper frequency edge of the UL Band more than 5.2 GHz Note 3: Applies for 2500-2690 MHz (n41 band) |

Table 22 Boundary between FR1 NR out of band and general spurious emission domain (see 3GPP TS 38.521-1 Table 6.5.3.1.3-1)

| Channel bandwidth | OOB boundary FOOB (MHz) |
| --- | --- |
| BWChannel | BWChannel + 5 |

Table 23 Spurious emissions Test Configuration Table for FR1 (see 3GPP TS 38.521-1 Table 6.5.3.1.4.1-1)

| Initial Conditions |
| --- |
| Test environment | Normal environment + normal voltage |
| Test Frequencies | Low range, Mid range, High range |
| Test channel bandwidth | Lowest, Mid, Highest |
| Subcarrier spacing | Lowest |
| Test parameters |
| Downlink Configuration | Uplink Configuration |
| Not applicable | Modulation | RB allocation (note) |
|  | CP-OFDM QPSK | OuterFull |
|  | CP-OFDM QPSK | Edge_1RB_Left |
|  | CP-OFDM QPSK | Edge_1RB_Right |
| Note: The specific configuration of each RB allocation is defined in 3GPP TS 38.521-1 Table 6.1-1. |

Table 24 Spurious emissions limits for FR2 (see 3GPP TS 38.521-2 Table 6.5.3.1.3-2)

| Frequency range | Maximum level | Measurement bandwidth | Note |
| --- | --- | --- | --- |
| 30 MHz ≤ f < 1000 MHz | -36 dBm | 100 kHz |  |
| 1 GHz ≤ f < 12.75 GHz | -30 dBm | 1 MHz |  |
| 12.75 GHz ≤ f ≤ 2nd harmonic of the upper frequency edge of the UL operating band in GHz | -13 dBm | 1 MHz |  |

Table 25 Spurious emissions Terminal co-existence limits for FR2 (see 3GPP TS 38.521-2 Table 6.5.3.2.3-1 and Table 5.2-1)

| NR band | Spurious emission |
| --- | --- |
|  | Protected band / frequency range | Frequency range (MHz) | Maximum level (dBm) | Resolution bandwidth (MHz) | Note |
| 28000 MHz band (27000 MHz-29500 MHz) | NR Band n260 (37000-40000MHz) | FDL_low (37000) | - | FDL_high(40000) | -2 | 100 |  |
|  | Frequency range (MHz) | 57000 | - | 66000 | 2 | 100 |  |
| Note: FDL_low and FDL_high refer to each NR frequency band specified in 3GPP TS 38.521-2 Table 5.2-1. |

Table 26 Limits for additional spurious emission for FR2 (see 3GPP TS 38.521-2 Table 6.5.3.3.3-1)

| Frequency range (GHz) | Maximum level (dBm) / Channel bandwidth | Measurement bandwidth | Note |
| --- | --- | --- | --- |
|  | 50MHz | 100 MHz | 200 MHz | 400 MHz |  |  |
| 23.6 ≤ f ≤ 24 | -8 | -8 | -8 | -8 | 200 MHz | 1 |
| Note 1: The protection of frequency range from 23.6 to 24 GHz is meant for protection of satellite passive services. |

Table 27 Test Configuration for FR2 spectrum emission mask (see 3GPP TS 38.521-2 Table 6.5.3.1.4.1-1)

| Initial Conditions |
| --- |
| Test environment | Normal environment + normal voltage |
| Test Frequencies | Low range, High range (note 2) |
| Test channel bandwidth | Highest |
| Subcarrier spacing | 120kHz |
| Test parameters |
| Test ID | Downlink Configuration | Uplink Configuration |
|  | Not applicable | Modulation | RB allocation (note 1) |
| 1 |  | DFT-s -OFDM QPSK | Inner_Full |
| 2 |  | DFT-s -OFDM QPSK | Inner_1RB (note 3) |
| Note 1: The specific configuration of each RB allocation is defined in 3GPP TS 38.521-2 Table 6.1-1. Note 2: When testing Low range test only in Frequency Range lower than (FUL_low – ΔfOOB) and when testing High range test only in Frequency Range higher than (FUL_high + ΔfOOB). Note 3: When testing Low range configure uplink RB to Inner_1RB_Left and when testing High range configure uplink RB to Inner_1RB_Right. |

Table 28 The Language of PWS Alert Contents of Message Identifier, Classification, Preset Receiving On or Off, and Options of Users, etc.

| Message identifier /Language of PWS alert contents | Classification | Default = activated or deactivated | Are users allowed to select receiving message identifier or deactivating? |
| --- | --- | --- | --- |
| 911/Chinese | 919/English | Alert Message | Default = receive | Yes |
| 4370/Chinese | 4383/English | Presidential Alert | Default = receive | No |
| 4371/Chinese | 4384/English | Emergency Alert | Default = receive | Yes |
| 4372/Chinese | 4385/English | Emergency Alert | Default = receive | Yes |
| 4373/Chinese | 4386/English | Emergency Alert | Default = receive | Yes |
| 4374/Chinese | 4387/English | Emergency Alert | Default = receive | Yes |
| 4375/Chinese | 4388/English | Emergency Alert | Default = receive | Yes |
| 4376/Chinese | 4389/English | Emergency Alert | Default = receive | Yes |
| 4377/Chinese | 4390/English | Emergency Alert | Default = receive | Yes |
| 4378/Chinese | 4391/English | Emergency Alert | Default = receive | Yes |
| 4379/Chinese | 4392/English | Emergency Alert | Default = receive | Yes |
| 4380/Chinese | 4393/English | Required Monthly Test | Default = deactivated | Yes |

Table 29 Device should produce corresponding audio signal and vibration cadence in accordance with the message identifier (MI) and the user’s setting.

| Message identifier | User’s setting |
| --- | --- |
|  | Deactivate sound | Activate sound | Deactivate vibration | Activate vibration |
| 911 | 919 | Can not produce audio signal | Produce audio general signal | Can not produce vibration cadence | Produce vibration general cadence |
| 4370 | 4383 |  | Produce audio attention signal |  | Produce vibration attention cadence |
| 4371 | 4384 |  |  |  |  |
| 4372 | 4385 |  |  |  |  |
| 4373 | 4386 |  |  |  |  |
| 4374 | 4387 |  |  |  |  |
| 4375 | 4388 |  |  |  |  |
| 4376 | 4389 |  |  |  |  |
| 4377 | 4390 |  |  |  |  |
| 4378 | 4391 |  |  |  |  |
| 4379 | 4392 |  |  |  |  |
| 4380 | 4393 |  |  |  |  |

Figure 1 Example of PWS Alert Content and Headers

Figure 2 Pattern of Audio Attention Signal

Figure3 Pattern of Vibration Attention Signal

# Text boxes

Your mobile phone operator complies with government policies and tests public warning. We apologize for any inconvenience and appreciate your kind understanding. National Communications Commission

Presidential Alert

NR 98%