Technical Specifications for the Telecommunications Terminal Equipment for DS1 Telecommunications

# National Communications Commission

# July 23 2020

Technical Specifications for the Telecommunications Terminal Equipment for DS1 Telecommunications

- Source of law

The Specifications are promulgated pursuant to Paragraph 1, Article 44 of the Telecommunications Management Act.

- Scope of application

The Specifications apply to digital signal 1 (DS1) telecommunications terminal equipment and only to general manufacturers, importers, vendors and private users.

- Test items and acceptance criteria

See the following table for test items and acceptance criteria.

Table DS1 Telecommunications Terminal Equipment Test Record

Brand: 					Model:

Test date:

| Test items | Acceptance criteria | Test result | Verdict |
| --- | --- | --- | --- |
| 1. Independent bodies other than those that shall be equipment for Type I telecommunications enterprises shall not be modified into equipment for Type I telecommunications enterprises. |  |  |  |
| The addition of equipment shall not compromise the exchange, testing and transmission performance of equipment for Type I telecommunications enterprises. |  |  |  |
| 3. The normal use of equipment for Type I telecommunications enterprises shall not be compromised when a piece of private equipment is not in use or malfunctions. |  |  |  |
| 4. A security device shall be provided if a piece of private equipment is operating on utility power (110/220V, 60Hz); the said may or may not be hidden in the said equipment. | FCC Part 68 of U.S.A. or equivalent |  |  |
| 5. Requirements for T-1 link aggregation interface | (1) Transmission rate of 1544 kb/s; (a) The tolerance for transmission rate deviation is ±50 ppm; (b) The tolerance for receiving rate deviation is ±50 ppm. |  |  |
|  | (2) The line code for link aggregation shall be Bipolar- AMI, 50% of duty cycle, and the requirements of pulse density no less than 12.5% and no more than 15 consecutive zeroes (0) shall be met; or the line code of B8ZS shall be used for link aggregation. |  |  |
|  | (3) The frame format shall be of D4 form or extended superframe; when ESF is provided, the format shall comply with the requirements of AT&T CB. No.142 and occupy no more than 4 kb/s of facility data link. |  |  |

Telecommunications Terminal Equipment Test Record (continued)

| Test items | Acceptance criteria | Test result | Verdict |
| --- | --- | --- | --- |
|  | (4) The pulse level shall comply with the suggestions of ITU-T G. 703 Pulse Mask for Interface at 1544 kb/s. |  |  |
|  | (5) The signal level shall comply with the suggestion of ITU-T G. 703 Digital Interface at 1544 kb/s. |  |  |
|  | (6) The test load impedance is 100Ω±5% (resistivity). |  |  |
|  | (7) The pulse imbalance is < 200mV for changes in signal amplitude and < 20ns for changes in pulse width. |  |  |
|  | (8) For jitter requirements, the requirement for signal jitters at the input and output of public telecommunications network DSX-1 signal interface shall be met. |  |  |
| 6. Clock synchronization | In addition to providing accuracy as the internal clock source for Stratum 4, private equipment shall be capable of extracting synchronization signal from T-1 network for the synchronization between signals and T-1 network for outgoing communications. |  |  |
| 7. Fault isolation capability | The link aggregation module of private equipment and channel modules shall be capable of self-testing and activated loop-back testing. |  |  |
| 8. Electric safety | Compliance with CNS 14336-1 |  |  |
| 9. Electromagnetic compatibility | Compliance with CNS 13438 |  |  |

| Final verdict | □ Accepted □ Not accepted |
| --- | --- |
| Function summary: |

Test body: supervisor: 		direct supervisor: 		test technician: